## Slide 1: CLUE design meeting discussion points

## Slide 2: CLUE/SDP division
SDP
Captures
Capture Scenes
Simultaneous Transmission Sets
Receiver selection of captures
CLUE channel
Encodings
Encoding Group Constraints
Receiver selection of encodings

## Slide 3: CLUE/SDP division
SDP
Captures
Capture Scenes
Simultaneous Transmission Sets
Receiver selection of captures
Encoding Group Constraints
CLUE channel
Encodings
Receiver selection of encodings

## Slide 4: Plan Z
Initial call-flow design with no changes to SDP
Separate m-line per send/receive stream
Separate 5-tuple per stream – no multiplexing

## Slide 5: Plan Z
Initial call-flow design with no changes to SDP
Separate m-line per send/receive stream
Separate 5-tuple per stream – no multiplexing
Required for disaggregated media case
Allows CLUE call-flow design to be separated from SDP multiplexing design
Later incorporate new multiplexing syntax

## Slide 6: Initial O/A: Offer
...
m=video 8000 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e016;max-mbps=108000;max-fs=3600
a=sendrecv
Initial offer, single video stream
Interoperable with legacy systems

## Slide 7: 2nd O/A: Offer
…
m=video 8000 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e01e
a=label:label1
a=sendonly
m=video 8002 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e01e
a=label:label2
a=sendonly
m=video 8004 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e01e
a=label:label3
a=sendonly
Can send up to three video streams

## Slide 8: CLUE Advertisement
Advertisement
Capture Scene 1
Capture 1: Spatial params <left camera>, Encoding Group 1
Capture 2: Spatial params <centre camera>, Encoding Group 1
Capture 3: Spatial params <right camera>, Encoding Group 1
Capture 4: Spatial params <switched>, Encoding Group 1
Capture Scene Entry: 1,2,3
Capture Scene Entry: 4
Simultaneous Sets: 1,2,3,4
Encoding Group 1: label1, label2, label3
Three-camera system
can send all three cameras
OR
can send single, switched stream

## Slide 9: 3rd O/A: Answer
m=video 8000 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e01e
a=label:label1
a=sendonly
m=video 8002 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e01e
a=label:label2
a=sendonly
m=video 8004 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e01e
a=label:label3
a=sendonly
m=video 8006 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e016;max-mbps=108000;max-fs=3600
a=label:foo
a=recvonly
m=video 8008 RTP/AVP 96
a=rtpmap:96 H264/90000
a=fmtp:96 profile-level-id=42e016;max-mbps=108000;max-fs=3600
a=label:bar
a=recvonly
Negotiate two receive video streams

## Slide 10: CLUE Configure
Configure
Stream foo: Remote Capture 100
Stream bar: Remote Capture 101
Associate receive streams with specific far-end captures

## Slide 11: What about encoding group constraints?

## Slide 12: Encoding Group Constraints The rationale
Represents limitations of real-world telepresence systems
Finite resources means it may not be possible to encode all streams at max resolution
Hardware limitations mean encoding resources may not be arbitrarily divisible

## Slide 13: Encoding Group Constraints The issues
<No specific codecs>
bandwidth

## Slide 14: Encoding Group Constraints The issues
<No specific codecs>
H264 baseline profile
bandwidth
max-mbps

## Slide 15: Encoding Group Constraints The issues
<No specific codecs>
H264 baseline profile
+ H264 high profile
+ H265
+ …
bandwidth
max-mbps
???
?!?!