## Slide 1: Provisioning IPv4 Configuration over IPv6 Only Networks draft-rajtar-dhc-v4configuration-01
B. Rajtar, I. Farrer
IETF 86, Orlando, March. 2013

## Slide 2: Motivation
From discussions at IETF85, there was an agreement to align the provisioning of IPv4 configuration parameters over IPv6 only networks
Main ‘customers’ for this are softwires (MAP-E, lw4o6) using DHCP based configuration
Currently, multiple possible approaches have been proposed using both DHCPv6 and DHCPv4 over IPv6, some implemented, but none standardized
The draft describes the proposed approaches listing their advantages and disadvantages
Aim is to have a single DHCP transport approach for all v4 over IPv6 networks

## Slide 3: DHCPv4o6 Based Provisioning
DHCPv4 messages are transported in UDP6/IPv6
Pros:
  Once implemented, all DHCPv4 parameters available without further development
  IPv4 and IPv6 provisioning can be separated
  Only minor adaptation to existing DHCPv4 flows
  If the address is leased, then the lifetime mechanism is built-in
Cons:
  New functional elements needed
  New DHCPv6 option is necessary (IPv6 address of the DHCPv4 server)
  DHCPv4 client and server must be updated to support the new function

## Slide 4: DHCPv6 Based Provisioning
DHCPv6 options are used to deliver all IPv4 config parameters
Pros:
  Simpler, in that no additional functional elements needed
  Single protocol used for all parameters
  Single provisioning point
Cons:
  All DHCPv4 options must be ported to DHCPv6 – re-development work is required
  All clients/servers need to be updated each time a DHCPv4 option is ported to DHCPv6
  In the future, ‘legacy’ IPv4 options will be kept in DHCPv6
  IPv4 and IPv6 domains not separated
  If the address is leased, then the lifetime mechanism needs to be brought into DHCPv6 as well

## Slide 5: DHCPv4 over Softwire Based Provisioning
IPv4 address is configured with DHCPv6. Other DHCPv4 messages are transported within an IPv6 tunnel in the same manner as any other IPv4 traffic
Pros:
  Once implemented, all DHCPv4 parameters available without further development
  Existing DHCPv4 and DHCPv6 architectures are used
  DHCPv4 and DHCPv6 can be separated for network flexibility if required
Cons:
  New functional elements needed
  Requires significant rework on existing softwire implementations
  DHCPINFORM not suitable for use over softwire
  Binds the deployment of IPv4 parameters with softwire implementations
  A new mechanism for configuring the client with the IPv4 unicast address of the DHCPv4 server is necessary

## Slide 6: Current Status
v00 published (with a CFA) with the conclusion that the DHCPv4 over IPv6 approach would be most suitable
This conclusion was the subject of some discussion on the mailing list
v01 was then issued with an empty conclusion section TBC with the overall view of the WG

## Slide 7: Next steps
Call for WG adoption
Agree the conclusion across the WG
Update other effected I-Ds (mainly softwire provisioning) in line with the outcome