## Slide 1: DIME WG IETF 86
Diameter Group Signaling
draft-ietf-diameter-group-signaling-00
Wednesday, March 13th, 2013
Lionel Morand

## Slide 2: Motivations
Reduce signaling in those use cases that require many Diameter sessions to be modified or terminated at the same time
Add group signaling to existing Diameter applications with minimal impact and ambiguity
Describe the problem space in an application neutral fashion (best practices?) to aid other SDOs in tackling this problem

## Slide 3: Two Problem Aspects
Managing group assignments
  How to add or remove sessions from groups
  Guidelines for modifying group assignments
Manipulating groups of sessions
  Defines new formatting of commands for group operations
  Defines rules how group operations can be applied to session state machines

## Slide 4: Document history & work item status
draft-ietf-dime-group-signaling-00 published in June 2012 (Expired)
Needs revision to reflect the WG's common view on how bulk signaling and operations can be accomplished
Discussion and evaluation of formatting options
Next: Progress draft towards stable state

## Slide 5: Brief Recap
2 approaches presented @IETF84
  dedicated Group Commands
  single Bulk Operations command
3rd approach proposed during the meeting
  re-using existing Diameter messages and command codes, with additional AVPs.
    Group-Session-ID AVP, Group-Session-Action AVP
  WG preferred approach

## Slide 6: Reusing Existing Commands: Overview
Working Assumptions:
  Minimal impacts on existing implementations
  Rely on command extensibility capability provided by the Diameter Base protocol.
  Reuse of existing commands will ease adoption
Existing command CCF are enhanced with optional [AVPs] providing support of group management
  e.g. Session-Group-Id AVP, Session-Group-Action AVP
When included in a command, it is up to the protocol designers to set or clear the M-bit.

## Slide 7: Reusing Existing Commands: NASREQ Example
Managing group assignments
  Session-Group-Id AVP (M-bit cleared) included in AAR, used to:
    indicate that the group management feature is supported by the NAS
      NAS not supporting the capability will not include the AVPs
    indicate the group Id assigned by the NAS to the session
  Session-Group-Id AVP (M-bit cleared) included in AAA, used to:
    indicate that the group management feature is supported by the server
      server not supporting the new AVPs will ignore those received in the request and not include these AVPs in the answer
    indicate the group Id assigned by the server to the session

## Slide 8: Reusing Existing Commands: NASREQ Example
Server initiated group re-auth/session abortion:
  Session-Group-Id and Session-Group-Action AVPs (M-bit cleared) included in RAR/ASR in addition to the session-id assigned to one of the user in the group
  the NAS performs the required action for the given session-id and the same action for the other user identified by the Session-Group-Id AVP
Client initiated group session termination
  Session-Group-Id and Session-Group-Action AVPs (M-bit cleared) included in STR
  the server performs the required action for the given session-id and the same action for the other user identified by the Session-Group-Id AVP

## Slide 9: Next Steps
Discussion initiated on the mailing list
  Setting of the M-bit?
  Use of the Session-Id AVP?
  Advertizing support of Group management?
  Link with Overload Control
Next Steps:
  Confirm interest for this work!!!
  Agree on working assumptions
  Produce a new version of the draft based on the agreed working assumptions