## Slide 1: Diameter Congestion And Filter Attributes
IETF 86, Orlando, USA
Lyle Bertz (lyle.t.bertz@sprint.com)
Brent Hirschman (brent.hirschman@sprint.com)
Supplement to
draft-bertz-dime-congestion-flow-attributes-00

## Slide 2: RFC 5777 Foundation
RFC 5777
Filter–Rule AVP
  The basis our work.
  Condition/Action design
Filter-Rule ::= < AVP Header: 509 >
[ Filter-Rule-Precedence ]
; Condition part of a Rule
; ------------------------
[ Classifier ]
* [ Time-Of-Day-Condition ]
; Action and Meta-Data
; --------------------
[ Treatment-Action ]
; Info about QoS related Actions
; ------------------------------
[ QoS-Semantics ]
[ QoS-Profile-Template ]
[ QoS-Parameters ]
[ Excess-Treatment ]
; Extension Point
; ---------------
* [ AVP ]

## Slide 3: Congestion Management
Filter-Rule does not support ECN in 2 ways
  No AVP to add to condition part to Classify ECN marked traffic
  No Congestion-Treatment Action Set (RFC has Excess-Treatment and Treatment-Action AVPs)
We need to build many filters for Congestion Management
  How do we know they are working? (Is any traffic captured)
  What can we observe on existing filters in order to remove unused ones OR ones deprecated by new filters?

## Slide 4: ECN Specific AVPs
ECN-IP-Codepoint AVP (Enumerated)
    Specifies the Explicit Congestion Notification codepoint values to match in the IP header.
    Use: Place in Filter-Rule’s Classifier
Congestion-Treatment AVP (Grouped)
    Similar in design/use to Excess-Treament AVP
    NOTE: Criteria for Congestion or traffic under congestion is out of scope of the AVP specification
  Flow-Count AVP (Unsigned64)
    Indicates the number of protocol specific flows. The protocol is determined by the filter
  Packet-Count AVP (Unsigned64)
    Indicates the number of protocol specific packets.

## Slide 5: Filter AVPs for maintenance
Two AVPs
  Flow-Count AVP (Unsigned64)
    Indicates the number of protocol specific flows. The protocol is determined by the filter
  Packet-Count AVP (Unsigned64)
    Indicates the number of protocol specific packets.
Uses
  Use in accounting/reporting to determine if Filter is working as planned
  Can be combined with other AVPs to provide rudimentary traffic profile (e.g. bytes per flow, bytes per packet, etc.)
  Can be sent in Filter-Rule as prescriptive

## Slide 6: Questions for Consideration
Should we add TCP ECE and CWR filters?
Should we add Classifier support for ECN for RTP over UDP (RFC 6679)?
What other extensions like RFC 6679 exist and should they be incorporated?