## Slide 1: I2RS Overlay usecase
Fangwei hu
Bhumip Khasnabish

## Slide 2: Goals
Two types Router in the I2RS network
  ER(Edge Router): Perform data encapsulation, topology and traffic report to control
  CR(Core Router): Simplicity and cost down, focus only on fast data forwarding
Provides an overlay structure
  Benefit:
    Lower cost down for Core Routers
    Improved network security
    Support of network virtualization

## Slide 3: Overlay Model
A
E
G
D
C
B
A
B
C
D
CR
CR
ER
ER
ER
ER
Physical topology
F
CR
Establishing IP/MPLS/OTN tunnel among ERs
ER encapsulate /decapsulate the data based on the tunnel type
CR only fast forward the encapsulation data
Logical tunnel

## Slide 4: Overlay Structure
Application
I2RS Client
ER
CR
Application
Application
I2RS Client
ER
CR
CR
Traffic analysis, path compute and route download to ER and CR
collect topology information and report to I2RS Client
LSA flood and topology announcement

## Slide 5: Core Router (CR): high capability, and simplicity
CR node(Core Node)：
  Mainly focus on fast forwarding of encapsulated data
  The control plane is very simple
    Topology announcement and flooding
    For compatibility, Route computing may need to be performed, but this may not necessary

## Slide 6: Edge Router (ER)
The Requirement for ER:
  Use Access authentication, authorization, and resource controller
  Topology management
  Policy management
  Route and signal protocol
  Tunnel management control
  Traffic analysis and report
  Service Management

## Slide 7: Network Virtualization (NV)
The ERs may support many services, and be complex
The Network Virtualization for ERs (control and forward elements virtualization)
  Reduce ER complexity and equipment costs
  Flexible and fast new services deployment
  Increase scalability and reliability
  Easy for function combination, achieving co-existence with hardware based network platform
  Rapid Service prototyping
  Service/Access agility

## Slide 8: Network Virtualization
Requirements (control and forward elements virtualization)
  Tunnel gateway elements: IPSec/SSL VPN gateway
  Traffic analytics: DPI, QoS measurement, SLA agent
  Converged and network-wide function: AAA Server, policy control and charging platform
  Security function: Firewalls, virus scanners, instruction detection and prevention systems, spam protection

## Slide 9: Overlay + Network Virtualization Structure
Core
Router/Switch
Edge Router
Core Router/Switch
Edge Router
Edge Router
Edge Router
Server
DPI
Server
FW
Server
NAT
Server
BRAS
I2RS
Client
Server
DPI
Server
FW
Server
NAT
Server
BRAS
I2RS
Client
Overlay network
The Server DPI(FW, NAT) is located in the application model in the I2RS structure

## Slide 10: Next Step
Comments and feedback?
Call for WG adoption?

## Slide 11
Thank you!!!!