## Slide 1: Functional Analysis of I2RS: What Are We Putting in the Mixture?
Alia Atlas
IETF 86, Orlando, FL

## Slide 2: Refining I2RS: the Feedback Loop
  Keep it reasonably scoped
  Don’t rush to the technology (but proto-typing could be useful)
New Functionality
Use-Cases
Use-cases justify and clarify the need for functionality
New Functionality triggers ideas for new Use-Cases

## Slide 3: It’s Just Like $foo Except…
Trying to capture what is new/different/critical
Concepts pulled from:
  draft-ward-i2rs-framework-00
  draft-atlas-i2rs-policy-framework-00
  draft-rfernando-irs-framework-requirement-00
  Other discussions

## Slide 4: The Basics
The NEED for SPEED
  ability to react in sub-second time
  Handled 100s, 1000s, etc. of operations
Reasonable Programmatic Interface for Network Applications
  Asynchronous
  Not >5 different protocols to accomplish a thing
  Pub/Sub model for Events

## Slide 5: Multi-Headed Control (motivation)
Multiple Clients (or Client + CLI) may want to write or modify the same state
  CLI comes in to override client application state
  Client application wants to override CLI (e.g. to enforce a policy)
  Use-Case: Large-flow router and DoS mitigation both identify the same flow/destination to route.
Depending on timing of processing of requests leads to unknown router state (which socket read first in a select, latency from an application)

## Slide 6: Multi-Headed Control (implications)
I2rs agent-based arbitration: enforce policy as to which client gets to modify contested state
  Store if not best (like RIB policy)
Client ownership: determines who can modify vs. delete/replace
Notifications on subscription when state is changed by another client
Optional garbage collection ephemeral state when client goes away

## Slide 7: Different Operation Models
Three characteristics to an operation:
  Start-Time (immediate, temporal, triggered)
  Persistence across reboots (permanent, ephemeral)
  Duration/State-expiration (unbounded, temporal)
CLI and Netconf generally give:
  Immediate, Permanent, Unbounded

## Slide 8: Subscriptions and Notifications
To be responsive to uncontrollable events, network applications learn via notifications
  Has state been overwritten?
  Has a next-hop changed?
  Has a threshold been passed?
  Has a route been installed?
Ability to filter and specify thresholds per subscription request.
Events and data-publication streams

## Slide 9: Multiple Transport Sessions
Different communications have different requirements
  Reliability, secrecy, replay, etc.
Clients and agents part of distributed systems
  A network application may be distributed to different locations.
  A network element may provide services via different system elements, want to distribute notifications and analytics from where they are learn or measured

## Slide 10: Role-Based Client Identity
An application can identify as a client even with:
  Different IP address
  Different TCP session
  Etc.
Supports distributed applications, standby for applications, etc.

## Slide 11: Client Limited Authorization
Ability to limit client ability to read and write based upon role.
  Can learn subset of topology
  Define write-scope in terms of values/ranges as well as data objects in model

## Slide 12: Client-Specific Priority
Client can specify a priority for each operation
  Allows in-flight and ASAP operations
  Operations across multiple channels can be put into desired order

## Slide 13: Standard Information and Data Models
RIB interactions:
  Static routes, redistribution into other protocols, varying admin-distance
  Variety of next-hop types
  Unicast, multicast, LFIB, etc.
BGP policy:
  Actions, etc.
IGP local policy
PIM local policy

## Slide 14: Topology
Varieties of Data
  Active IGP topology
  Active components (e.g. customer or peer links)
  Passive components (can be detected)
  Passive components (undectable)
  Minimal historical (last up, last peer, etc.)
Network Abstractions
  Service points-of-presence
  VPN topologies
  unsummarized topology

## Slide 15: Motherhood and Apple-Pie: Pick Your Recipe
Atomic Operations
Preemptable Locking: take ownership at precedence for blocking changes or to write
Rollback by client
Capabilities
Optional garbage collection

## Slide 16: Flexible Components to Consider
Data Modeling Language
Protocol
Transfer Syntax
Transport
YANG, ASN.1
XML, Google ProtoBufs,
Binary
NetConf,
XMPP
TCP, UDP, TLS,
SCTP

## Slide 17: What to keep?
Some functionality drives and determines the architecture…
Some can be added later…
Need to justify with use-cases and consensus
TIME to DISCUSS