## Slide 1
draft-ietf-idr-ls-distribution-02
Hannes Gredler – hannes@juniper.net
Jan Medved – jmedved@juniper.net
Stefano Previdi – sprevidi@cisco.com
Adrian Farrell – adrian@olddog.co.uk
Saikat Ray – sairay@cisco.com
Thanks to:
Nischal Sheth, Alia Atlas, David Ward, Derek Yeung, Murtuza Lightwala, John Scudder, Kaliraj Vairavakkalai, Les Ginsberg, Liem Nguyen, Manish Bhardwaj, Mike Shand, Peter Psenak, Rex Fernando, Richard Woundy, Steven Luong, Tamas Mondal, Waqas Alam, Vipin Kumar, Naiming Shen and Yakov Rekhter
IETF 86 Orlando, March 2013

## Slide 2: draft-ietf-idr-ls-distribution-02
Scope:
  Advertisement of link-state topology information in new BGP NLRIs and Attributes
  Definition of a common topology abstraction model for carrying both OSPF and/or ISIS original LSDBs
  Deliver topology information to topology servers, orchestration elements, ALTO servers, etc, residing outside the routing layer and requiring network topology information
  Allow the manipulation of topology information through aggregation, hiding, abstraction, etc.
  Allow a topology server to reconstruct the end-to-end topology view based on multiple BGP-LS feeds.
Out of scope:
  Leak link-state information back into the routing layer
  Use BGP-LS for installing state into routers
Details on Motivation and Applicability of BGP-LS are explained in Section 2

## Slide 3: draft-ietf-idr-ls-distribution-02
BGP-LS Speaker
BGP-LS RR
BGP-LS Speaker
ALTO
PCE
IGP Redistribution into BGP-LS
Advertisement of BGP-LS NLRIs to RR
Advertisement of BGP-LS NLRIs to Topology Servers, PCEs, ALTO servers, …
Topology Server

## Slide 4: draft-ietf-idr-ls-distribution-02
New Address Family: AFI/SAFI TBD
New NLRI: BGPLS NLRI
“NLRI Type” field
Section 3.2: NLRI format
  0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | NLRI Type | Total NLRI Length |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | |
  | Link-State NLRI (variable) |
  | |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  Figure 1: Link State SAFI 1 NLRI Format

## Slide 5: draft-ietf-idr-ls-distribution-02
NLRI Type allows multiple NLRI formats within BGP-LS AFI/SAFI
Following are currently defined
  Type = 1: Link NLRI, contains link descriptors and link attributes
  Type = 2: Node NLRI, contains node descriptors and node attributes
  Type = 3: IPv4 Topology Prefix, contains IPv4 prefix descriptors and attributes
  Type = 4: IPv6 Topology Prefix, contains IPv4 prefix descriptors and attributes
More to come: TE-LSPs

## Slide 6: draft-ietf-idr-ls-distribution-02
Operations
  No changes in BGP procedures
    Loop prevention and path selection
  BGP Path selection rules apply
    May be used by receiver to prefer given source

## Slide 7: draft-ietf-idr-ls-distribution-02
Updates to the 02 version
Identifier TLV:
  Instance, Domain, Area, OSPF Route Type and Multi-Topology identifiers are all encoded in the Identifier TLV
Clarity in the text about Descriptors and Attributes
  For Node, Link and Prefixes
Fixed inconsistencies in terms of Area/Router/Link/Prefix Identifiers
Added prefix attributes
Added table summarizing all TLVs and SubTLVs

## Slide 8: draft-ietf-idr-ls-distribution-02
Three implementations
Interoperability tests planned very soon

## Slide 9: draft-ietf-idr-ls-distribution-02
Thank You