## Slide 1: Advanced Stream and Sampling Framework for IPPM draft-morton-ippm-2330-update-01
Joachim Fabini and Al Morton
March 2013

## Slide 2: Status & Motivation
Networks have evolved
  RFC 2330 assumes linear network behavior (“wire“)
  Smart networks: Measurement results depend to a large extent on measurement stream (on-demand allocation)
  RFC 2330 metric and methodology properties are a useful theoretical instrument - limited in real life now (repeatability)
  Network-internal flow state at layers below IP
Proposal: Update 2330
Notes: Diagram: round-trip delay measurements in HSPA network, random payload and random start-time, 35+ hours of measurements, 50K samples

## Slide 3: Scope of Advanced Framework
Describe useful additional stream parameters
  Restore repeatable measurements in modern networks
Aspects
  1. Network treatment depends on Type-P (concept ext.)
  2. Packet history influences network/results
  3. Access technology may change during session
  4. Time-slotted service time in network paths

## Slide 4: Main Comment: Define “Reactive Network”
Sec 1.1 Reactive Network Behavior
  Sensing packet arrival/inactivity for a flow of interest
  Assessment intervals or multiple arrivals
  Result in new mode of operation in one or more network components
  Deterministic/Observable w.r.t. the flow of interest
  Defined at a particular layer (e.g., reactive at IP layer)
A network or path is said to be reactive when at least one link or host on the path exhibits reactive behavior

## Slide 5: Examples: Reactive Behavior
Layer Independent:
Link establishment in response to flow activity
  This is why a concept of pre-test load is needed
Channel capacity adaptation
  Decision to increase or decrease capacity on a sub-IP link based on past or current flow rate.
  Decision to use signaling channel for sporadic, small data packets instead of allocating dedicated bearer
Layer Dependent:
Link-level compression of packet payload(s) depending on Type-P and higher-layer content
  For instance JPEG file downsizing and –scaling in mobile networks (server-side optimizers)
Content-based interception

## Slide 6: Examples: NON-Reactive Behavior
“Green” features
  Activate idle fiber link when Util>X
  Deactivate fiber link when Util<Y
Policies triggering on total cell load
  Mobile networks: bias of capacity allocation algorithms by current total cell load (all users)
Channel adaptation between low-capacity or high-capacity on a sub-IP link appears random.
  Fall-back to accommodate appearance of a legacy device
  Signal quality (lower-layers, position, interference)
  Activating or de-activating a dedicated VC on an xDSL link (e.g., some DSL modems do this when switching on or off a VoIP phone or an IPTV box, substantially reducing the capacity available for best-effort traffic).

## Slide 7: Summary Status and Discussion
Detailed discussion on the mailing list (2012)
Support to do the work
Adopt as a working group item?
Possible future work: Define methods to test for reactive network behavior, based on fundamental IPPM metrics

## Slide 8: Backup

## Slide 9: Measurement Methodology & Setup
End-to-end ICMP round-trip delay measurements
Initiated by UE (mobile client), reflected by server
Client and server synchronous with global time (PPS, ~10µs).
Randomness in space and time
  Packets having random payload size are sent out at random start times

## Slide 10: 1. Expand elements of Type-P 2. Packet History Influence
Test packet length
Content optimization
Flow state: multi-modal distributions
Notes: Diagram: uplink delay measurement in HSPA network, 35+ hours of measurements, 50K samples

## Slide 11: 3. Access Technology Change (App-transparent)
Applications might not detect changes
Overlayed
Mobile measurements (LMAP)
Representativeness?
Notes: Diagram: uplink delay measurement in HSPA+LTE network, 6 hours of measurements, 40K samples (artifically overlayed)

## Slide 12: 4. Time-slotted Networks
First time-slotted segment cancels randomness
Biased samples lead to multi-modal delay distributions
Notes: Diagram: downlink delay in HSPA network, 3+ hours of measurements, 20K samples
Left: unbiased samples. Right: biased samples (extracted from round-trip delay samples: uplink is time-slotted, therefore downlink measurement samples are biased – interaction with downlink timing)

## Slide 13: IPPM Feedback on the list
Matt Mathis
  Add “actionable” metrics
  Pre-test load – special aspect of “packet history”?
Rüdiger Geib, Matt Mathis
  Characterization of special treatments
    Traffic shaping
    Flow suppression
  Add as subtopic under Test Packet Type-P
  Define “reactive network behavior”
  Discussion of test traffic preferences in the wild

## Slide 14: Goals – Next Steps
Metric & Methodology properties:
  Improve Repeatability, Continuity, Extensibility
  Can/should we formalize these properties?
  Assess “Quality of Measurement” to evaluate if properties are satisfied for two measurement sample sets?
  Aim: find minimum set of parameters such that measurements have one or several of the above-mentioned properties.
Classification: methodology-invariant metrics?