## Slide 1: A registry for IPPM metrics
draft-bagnulo-ippm-new-registry-00
draft-bagnulo-ippm-new-registry-independent-00
M. Bagnulo, T. Burbridge S. Crawford, P. Eardley, A. Morton

## Slide 2: Motivation
Allow a Controller to request a Measurement Agent to perform a specific test
Allow a Measurement Agent to report the results of a specific test to a Collector.
Protocol Independent registry: Allows multiple protocols to be defined between Controller, Measurement Agents and Collector
  e.g. IPFIX between the MA and the Collector and YANG/NETCONF between the Controller and MA
  This may requires additional protocol specific fields

## Slide 3: Well-defined and operational metrics
RFC4148 defined an IPPM metric registry
RFC6248 obsoleted RFC4148
  it was "found to be insufficiently detailed to uniquely identify IPPM metrics... [there was too much] variability possible when characterizing a metric exactly”
New registry: tightly defined metric with few open parameters (don’t affect the nature of the test)
  e.g. source and dest address and the like
Less is more: reduced number of metrics proven useful
  We require both specification AND expert review for new assignments
  Specification covers the well defined and expert review the operational
Side benefits:
  Inventory of useful and used metrics
  Comparable test results even if performed by different implementations and in different networks

## Slide 4: Information to be conveyed
"Dear measurement agent: Please start test RTT(server.com,150) every day at 2000 GMT. Run RTT test every 1 second for 50 times. Do that when the network is idle. Generate both raw results and 99th percentile mean. Send measurement results to collector.com in IPFIX format".

## Slide 5: Registries
The commnly used metric registry
  Scheduling registry
  Environment registry
  Output-type registry
  Metric registry

## Slide 6: Scheduling Registry
Defines the scheduling strategy for the metric
  Initial allocations
    Singleton (additional input time of execution)
    Periodic (additional parameters, initial time, end time and rate)
    Poisson (additional parameters, initial time, end time and rate)

## Slide 7: Environment Registry
Defines the conditions where the metric is to be executed.
  Initial allocations
    Undefined: no additional environment settings are provided
    No-cross traffic: The "No cross traffic" condition is satisfied when, during the 5 seconds preceding measurement of the metric:
      the level of traffic flowing through the interface that will be used to send measurement packets in either direction is less than a threshold value of 1% of the line rate of the aforementioned interface.

## Slide 8: Output-type Registry
Defines the type of output the metric produces, either raw or some statistics.
  Initial allocations
    Raw: the raw output of the test
    Xth percentile interval
    Xth percentile mean

## Slide 9: Metric Registry
Two approaches:
  Independent registries, the metric being one more
    The metric registry entries are simply metric IDs
    A test is defined with as the tuple (metric, scheduling, Output-type, Environment)
    Possible explosion (implementation side) due to combinations
  Sub-registries of the metric registry.
    Each entry of the metric registry fully defines a test
    The metric registry has the following entries:
      Metric ID
      Scheduling (value out of the Scheduling sub-registry)
      Output-Type (value out of the Output-Type sub registry)
      Environment (value out of the Environment sub registry(
    Combinations are defined explicitly, possible explosion of entries

## Slide 10: Metric registry
Initial Allocations (inspired in MBA report):
  UDP latency
  UDP packet loss
  ICMP packet loss
  DNS latency
  VOIP latency
  VOIP loss
  VOIP Jitter