## Slide 1: Flooding Scope PDUs draft-ginsberg-isis-fs-lsp-00.txt
Les Ginsberg (ginsberg@cisco.com)
Stefano Previdi (sprevidi@cisco.com)
Yi Yang (yiya@cisco.com)

## Slide 2: What Problems are being addressed
  Reliable Link Scoped Flooding
    Efficient/Reliable flooding of information only of interest to routers on a given link
    Scalable
    TRILL AF information
  Extending LSP Space
    Existing solution (RFC 5311) is backwards compatible but…
      Requires multiple system ids
      Restricts TLV advertisements
    New solution removes restrictions – but not backwards compatible
  Support of New Flooding Scopes
    Domain-wide Flooding Scope
    More flexible/scalable than Router Capability TLV

## Slide 3: Overview
  Introduce a new LSP with flooding scope encoded in the LSP header (also new CSNP/PSNP)
  Minimize the use of limited PDU type space
  Define new flooding scopes
  LSPs for each scope are kept in a scope specific LSDB
  Not backwards compatible

## Slide 4: FS-LSP
Intradomain Routeing Protocol Discriminator |  |  |  |  |  | 
Length Indicator |  |  |  |  |  | 
Version/Protocol ID Extension |  |  |  |  |  | 
ID Length |  |  |  |  |  | 
R |  | R |  | R | PDU Type | 
Version |  |  |  |  |  | 
Reserved |  |  |  |  |  | 
Maximum Area Addresses |  |  |  |  |  | 
PDU Length |  |  |  |  |  | 
Remaining Lifetime |  |  |  |  |  | 
LSP ID |  |  |  |  |  | 
Sequence Number |  |  |  |  |  | 
Checksum |  |  |  |  |  | 
P | ATT |  | LSPDBOL |  |  | IS Type
VARIABLE LENGTH FIELDS |  |  |  |  |  | 
Intradomain Routeing Protocol Discriminator |  |  |  |  |  | 
Length Indicator |  |  |  |  |  | 
Version/Protocol ID Extension |  |  |  |  |  | 
ID Length |  |  |  |  |  | 
R |  | R |  | R | PDU Type | 
Version |  |  |  |  |  | 
Reserved |  |  |  |  |  | 
Flooding Scope |  |  |  |  |  | 
PDU Length |  |  |  |  |  | 
Remaining Lifetime |  |  |  |  |  | 
LSP ID |  |  |  |  |  | 
Sequence Number |  |  |  |  |  | 
Checksum |  |  |  |  |  | 
P | ATT |  | LSPDBOL |  |  | IS Type
VARIABLE LENGTH FIELDS |  |  |  |  |  | 
R| Scope (1 – 127)
Flooding Scope (8 bits)
Source ID
Pseudonode ID
LSP Number
ID Length
1 Octet
1 Octet
Standard Format
Source ID
Extended LSP Number
ID Length
2 Octets
Extended Format
Standard LSP Header
FS- LSP Header

## Slide 5: FS-CSNP
R| Scope (1 – 127)
Flooding Scope (8 bits)
Intradomain Routeing Protocol Discriminator |  |  | 
Length Indicator |  |  | 
Version/Protocol ID Extension |  |  | 
ID Length |  |  | 
R | R | R | PDU Type
Version |  |  | 
Reserved |  |  | 
Maximum Area Addresses |  |  | 
PDU Length |  |  | 
Source ID |  |  | 
Start LSP ID |  |  | 
End LSP ID |  |  | 
VARIABLE LENGTH FIELDS |  |  | 
Intradomain Routeing Protocol Discriminator |  |  | 
Length Indicator |  |  | 
Version/Protocol ID Extension |  |  | 
ID Length |  |  | 
R | R | R | PDU Type
Version |  |  | 
Reserved |  |  | 
Flooding Scope |  |  | 
PDU Length |  |  | 
Source ID |  |  | 
Start LSP ID |  |  | 
End LSP ID |  |  | 
VARIABLE LENGTH FIELDS |  |  | 
FS- CSNP Header
Standard CSNP Header

## Slide 6: FS-PSNP
U| Scope (1 – 127)
Flooding Scope (8 bits)
Intradomain Routeing Protocol Discriminator |  |  | 
Length Indicator |  |  | 
Version/Protocol ID Extension |  |  | 
ID Length |  |  | 
R | R | R | PDU Type
Version |  |  | 
Reserved |  |  | 
Maximum Area Addresses |  |  | 
PDU Length |  |  | 
Source ID |  |  | 
VARIABLE LENGTH FIELDS |  |  | 
Intradomain Routeing Protocol Discriminator |  |  | 
Length Indicator |  |  | 
Version/Protocol ID Extension |  |  | 
ID Length |  |  | 
R | R | R | PDU Type
Version |  |  | 
Reserved |  |  | 
Flooding Scope |  |  | 
PDU Length |  |  | 
Source ID |  |  | 
VARIABLE LENGTH FIELDS |  |  | 
U = 1 => Flooding Scope Not Supported
  Used to suppress retransmission of unsupported scopes on Pt-Pt circuits
Standard PSNP Header
FS-PSNP Header

## Slide 7: Announcing Supported Scopes
Announcement is optional – useful to detect misconfigs
Does NOT affect adjacency formation
Announce list of supported scopes in IIHs
Include:
  Circuit scopes supported on that circuit
  Non-circuit scopes supported on that circuit
  L1 IIH includes L1 scopes and domain scopes
  L2 IIH includes L2 scopes and domain scopes
  Pt-Pt IIH includes scopes for the levels supported on that circuit as well as domain scopes
New TLV
+----------------------+
|R| Supported Scope | 1
+----------------------+
: :
+----------------------+
|R| Supported Scope | 1
+----------------------+

## Slide 8: Update Process Operation
One instance of Update Process for each supported scope
Normal operation – but operates only on circuits supporting the given scope
One LSDB per scope
Point-to-Point Circuits
  Receipt of PSNP w U bit set in scope suppresses retransmission of LSPs w that scope
  Only occurs in mismatched configuration
Broadcast Circuits
  No changes to DIS election
  No Scope specific DIS
  Scopes which are not level specific are flooded by both L1 and L2 (if supported)

## Slide 9: Scope Types
  Circuit Scopes
    Local to a given circuit
    Receivers do NOT flood on any other circuit
    L1/L2 specific
  L1/L2 Scope
    Flooding domain identical to existing L1/L2 LSPs
  Domain-wide Scope
    Flooded on all circuits
    Check reachability using Router ID TLVs

## Slide 10: Deployment Considerations
New PDUs will not be recognized by legacy implementations
Legacy implementations likely to treat unknown PDU type as an error
Partial deployment is possible
Only routers within a given flooding scope have to support the new PDUs
Only routers within a given flooding scope have to support that flooding scope
Use of U bit in PSNP helps w partial deployment – but behavior may be unpredictable