## Slide 1: IS-IS Support for Unidirectional Links draft-ginsberg-isis-udl-00.txt
Les Ginsberg (ginsberg@cisco.com)
Sina Mirtorabi(smirtora@cisco.com)
Stefano Previdi (sprevidi@cisco.com)
Abhay Roy(akr@cisco.com)

## Slide 2: Goals
Modest Protocol Extensions
No IP Encapsulation
No Static Configuration of neighbor Information
Allow UDL on the Return Path
Reliable Adjacency Maintenance
Reliable LSP Updates
Minimum Additional Network Wide Protocol Traffic
Support for Pt-Pt and LAN subnetworks

## Slide 3: Basic Mechanisms
  Sending Hellos
    IS-T sends hellos as normal
    IS-R sends hello information in “UDL-LSPs”
  Adjacency Maintenance
    IS-T relies on existence of return path rooted at IS-R to IS-T
    IS-R maintains as normal
  Update Process
    IS-T operates as DIS on LAN (even on Pt-Pt links)
    IS-R operates as non-DIS on LAN (even on Pt-Pt links)
    IS-R may use UDL-LSPs to send PSNP equivalent
    Special rules for UDL-LSPs

## Slide 4: UDL-LSPs
Must be a non-zero fragment
Contains only UDL TLVs [and authentication/purge TLVs]
Enforcement by sender (not checked by receiver)
Flooded normally…some exceptions on UDL Circuits
UDL-LSPs flooded on UDL Circuits regardless of adjacency state (allows formation of adjacency on UDL even when return path is via a UDL)

## Slide 5: UDL-TLV
# octets
+---------------------------+
| Type (11) | 1 | (To be assigned by IANA) |
+---------------------------+
| Length | 1
+---------------------------+
| Sub-TLVs | 3 - 255
: :
+---------------------------+
Sub-tlv Types
Pt-Pt IS-Neighbor
LAN IS-Neighbor
LSP Entries
Manual Area Addresses

## Slide 6: IS-Neighbor sub-TLV
Pt-Pt IS-Neighbor
# octets
+---------------------------+
| Type (240) | 1 | (To be assigned by IANA) |
+---------------------------+
| Length (9+ID Length) to | 1
| (15 + ID Length) |
+---------------------------+
| Adjacency 3-way state | 1
+---------------------------+
| Extended Local Circuit ID | 4
+---------------------------+
| Neighbor System ID | ID Length
+---------------------------+
| Neighbor Extended Local | 4
| Circuit ID |
+---------------------------+
| Local LAN Address | 6
| | (LAN only)
+---------------------------+
LAN IS-Neighbor
# octets
+---------------------------+
| Type (6) | 1 | (To be assigned by IANA) |
+---------------------------+
| Length (7 + ID Length) | 1
+---------------------------+
| Neighbor LAN ID | ID Length+1
+---------------------------+
| Local LAN Address | 6
+---------------------------+

## Slide 7: LSP Entry sub-TLV
Sub-TLV Format
# octets
+---------------------------+
| Type (9) | 1 | (To be assigned by IANA) |
+---------------------------+
| Length (10+ID Length) *N | 1
+---------------------------+
: LSP Entries :
+---------------------------+
LSP Entry
# octets
+---------------------------+
| Remaining Lifetime | 2
+---------------------------+
| LSP ID | ID Length + 2
+---------------------------+
| LSP Sequence Number | 4
+---------------------------+
| Checksum | 2
+---------------------------+

## Slide 8: Manual Area Address sub-TLV
Sub-TLV Format
# octets
+---------------------------+
| Type (1) | 1 | (To be assigned by IANA) |
+---------------------------+
| Length | 1
+---------------------------+
: Area Address(es) :
+---------------------------+
Area Address
# octets
+---------------------------+
| Address Length | 1
+---------------------------+
| Area Address | Address Length
+---------------------------+

## Slide 9: Simple UDL Topology – Pt-Pt Adjacency Establishment
T sends P2P-IIH (State Init, Local Cid n)-> R
R sends UDL-LSP (State Init, Local Cid p, Neighbor T, Neighbor Cid n, [Local LAN Address])
UDL-LSP Propagated by B to T
T sends P2P-IIH (State UP, Local Cid n, Neighbor R, Neighbor Cid p)
R sends UDL-LSP (State UP, Local Cid p, Neighbor T, Neighbor Cid n, [Local LAN address])
T sends CSNPs to R
T floods LSPDB to R (once)
R
T
B

## Slide 10: Simple UDL Topology – Pt-Pt Adjacency Establishment w UDL in return path
T sends P2P-IIH (State Init, Local Cid n)-> R
R sends UDL-LSP (State Init, Local Cid p, Neighbor T, Neighbor Cid n, [Local LAN Address])
UDL-LSP Propagated by B to T even when adjacency is in INIT state
T sends P2P-IIH (State UP, Local Cid n, Neighbor R, Neighbor Cid p)
R sends UDL-LSP (State UP, Local Cid p, Neighbor T, Neighbor Cid n, [Local LAN address])
T sends CSNPs to R
T floods LSPDB to R (once)
R
T
B

## Slide 11: Simple UDL Topology – LAN Adjacency Establishment
T multicasts LAN-IIH (LANID T-n)
Rn sends UDL-LSP (LANID T-n, Local LAN Address]) and creates adjacency in Init state
UDL-LSPs Propagated by B to T
T creates adjacency(s) in UP state, sends LAN-IIH (LANID T-n, LAN Address R1, LAN Address R2…)
Rn transition adjacency to UP state
T sends CSNPs to LAN
T floods LSPDB to LAN
T
R1
B
R2
Splitter

## Slide 12: Adjacency Maintenance – P2P - Transmit Side
T sends periodic P2P-IIH (State UP, Local Cid n, Neighbor R, Neighbor Cid p)
T maintains adjacency with R so long as:
It has valid UDL-LSP from R with adjacency info (State UP, Local Cid p, Neighbor T, Neighbor Cid n, [Local LAN address])
T can calculate a return path from R to T which does NOT use the UDL circuit
Return path calculation is only required when a topology change occurs
R
T
B

## Slide 13: Adjacency Maintenance – P2P - Receive Side
R maintains adjacency based on receipt of periodic P2P-IIH (State UP, Local Cid n, Neighbor R, Neighbor Cid p) as normal
R
T
B

## Slide 14: Adjacency Maintenance – LAN –TX Side
T
R1
B
R2
Splitter
T sends periodic LAN-IIH (LANID T-n, LAN Address R1, R2…)
T maintains adjacency with Rn so long as:
  It has valid UDL-LSP from Rn with adjacency info (LANID T-n, Local LAN address Rn)
  T can calculate a return path from Rn to T which does NOT use the UDL circuit
Return path calculation is only required when a topology change occurs

## Slide 15: Adjacency Maintenance – LAN –RX Side
T
R1
B
R2
Splitter
Rn maintains adjacency based on receipt of periodic LAN--IIH (LANID T-n, IS Neighbor LAN Address Rn as normal

## Slide 16: Adjacency Failure Detection: Case #1
UDL Link between T-R fails
Adjacency Holddown timer on R times out – adjacency on R is down
R sends UDL-LSP w no UDL neighbor T information
T receives updated UDL-LSP – takes adjacency to R down
R
T
B
X

## Slide 17: Adjacency Failure Detection: Case #2
R
T
B
X
Link between B-R fails
B generates new LSP w no neighbor info to R
T receives updated LSP from B
T recalculates return path from R to T – takes adjacency to R down
T sends P2P-IIH (State Init, Local Cid n)-> R
R takes adjacency to T down
R generates UDL-LSP (State Init, Local Cid p, Neighbor T, Neighbor Cid n, [Local LAN Address])

## Slide 18: Update Process Overview
R
T
B
Flooding process is the same on P2P and LAN cases except for destination address
For LSP flooding, T operates on the circuit in a manner similar to a LAN where T is the DIS:
Send new LSPs once only (no ACK expected)
Periodic CSNPs
PSNP requests for LSPs embedded in the UDL-LSP from R will cause a retransmission
For LSP reception, R operates on the circuit as a non-DIS on a LAN.
Does NOT send acknowledgements
May send PSNP requests in its UDL-LSP for LSPs it sees in CSNPs from T
Delay before sending PSNP to minimize need to utilize UDL-LSP for this purpose (network-wide flooding)

## Slide 19: Update Process Pathological Example
R
T
B
New LSP A-00(20) arrives @ T
T floods LSP A-00(20) to R
R fails to receive LSP A-00(20)
T sends periodic CSNP to R showing A-00(20)
R sends PSNP for A-00(20) in a UDL-LSP to B
B receives UDL-LSP from R and floods to T
T receives UDL-LSP R via B and processes PSNP entry
T retransmits LSP A-00(20) to R
R receives LSP A-00(20), updates database
Steps 2-8 repeat if necessary until successful update.

## Slide 20: Update Process UDL Special Rules
T sends P2P-IIH (State Init, Local Cid n)-> R
R sends UDL-LSP (State Init, Local Cid p, Neighbor T, Neighbor Cid n, [Local LAN Address])
UDL-LSP Propagated by B to T even when adjacency is in INIT state
T fails to receive UDL-LSP
B periodically transmit R’s UDL-LSP until it can calculate return path from R to T
T receives R’s UDL-LSP…adjacency comes up
B stops periodic retransmissions of R’s UDL-LSP
R
T
B

## Slide 21: UDL Metrics
R
T
B
10
Max
R
T
B
10
Max
Unicast
Multicast