## Slide 1: draft-boutros-l2vpn-evpn-vpws-01.txt Sami Boutros Ali Sajassi Samer Salam John Drake Jeff Tantsura IETF 86, March 2013 Orlando, Florida

## Slide 2: Changes from 00 01
Added new authors, John and Jeff.
Added a new attribute ESI Bandwidth attribute.

## Slide 3: How it works?
The EVPN ability to forward customer traffic to/from a given customer Attachment Circuit (aka Ethernet AD route) is ideal in providing P2P services (aka VPWS services).
EVPL can be considered as a VPWS with only two ACs. Traffic forwarding capability of E-VPN between a pair of Ethernet AD routes is used.
MPLS label associated with the destination Ether AD route can be used in forwarding user traffic to the destination AC.

## Slide 4: ESI Bandwidth Attribute
+----------------------------------------------+
| Type (2 octets) |
+----------------------------------------------+
| Length (2 octets) |
+----------------------------------------------+
| Flags (1 Octet) |
+----------------------------------------------+
| Reserved=0(1 Octet) |
+----------------------------------------------+
| Reverse SENDER_TSPEC |
+----------------------------------------------+
The content of the SENDER_TSPEC are as defined in [RFC 2210] section 3.1.
The PE that receives this attribute MUST request the appropriate resources described in the SENDER_TSPEC from PSN.
In the case where PSN resources are not available, the receiving PE MUST re-send its local Ethernet AD routes for this with the Flags set to 1 "PSN Resources Unavailable”.

## Slide 5: Next steps
Comments are appreciated.
Thank you