## Slide 1: VXLAN DCI Using EVPN draft-boutros-l2vpn-vxlan-evpn-01.txt Sami Boutros Ali Sajassi Samer Salam Dennis Cai IETF 86, March 2013 Orlando, Florida

## Slide 2: VXLAN DCI Using EVPN
This is to provide intra-subnet connectivity at Layer 2 and control-plane separation among the interconnected VXLAN or NVGRE networks over the EVPN MPLS/IP network.
  The scope is limited to data plane learning in this document.

## Slide 3: Requirements
Control Plane Separation among VXLAN/NVGRE Networks.
Layer 2 Extension over the MPLS/IP Network for intra-subnet connectivity.
Support for IRB for both inter-subnet routing and intra-subnet bridging for a given VNI/VSID.

## Slide 4: Solution overview
  +-----------------+
  | |
  +-----------+ +-----+ MPLS +------+ +----------+
  +--------+ | |---|PE1 | |PE3 |--| | +---------+
  |VTEP1|--| | +------+ +------+ | |--|VTEP3|
  +--------+ | VXLAN | +------+ +------+ | VXLAN| +--------+
  +--------+ | |---|PE2 | |PE4 |--| | +--------+
  |VTEP2|--| | +------+Backbone+------+ | |--|VTEP4|
  +--------+ +-----------+ +--------------+ +---------+ +--------+
  |<------ IGP ------------->|<-----BGP-------------->|<------ IGP ---------->| CP
  |<----- VXLAN --------->|<EVPN/PBB-EVPN>|<------ VXLAN ------->| DP
  |<----MPLS----->|
  Legend: CP = Control Plane View DP = Data Plane View

## Slide 5: EVPN Routes
BGP MAC/B-MAC Advertisement Route for EVPN/PBB-EVPN
Ethernet Auto-Discovery Route for EVPN
Per VPN Route Targets
Inclusive Multicast Route to distribute the VNI information over the MPLS network.
  Discovery of the PEs participating in a given VNI.
  Stitching of the IP multicast trees, local to each VXLAN site, with the Label Switched Multicast (LSM) trees of the MPLS network.

## Slide 6: Handling Unicast traffic
Host MAC addresses will be learnt in data plane from the VXLAN network.
Host MAC addresses will be learnt over the MPLS/IP core:-
  In control plane for EVPN.
  In data plane [in case of PBB-EVPN].
L2 Unicast traffic destined to the VXLAN network will be encapsulated with the IP/UDP header+Customer bridge VNI.
L2 Unicast traffic destined to the MPLS/IP network will be encapsulated with the MPLS label.

## Slide 7: Handling Mcast traffic
Each VXLAN network independently builds its P2MP or MP2MP shared multicast trees for one or more VNIs.
In the MPLS/IP network, multiple options are available for the delivery of multicast traffic:
  Ingress replication
  LSM Options.
The stitching must ensure for MH VXLAN network:
  No Packet Duplication
  No Forwarding Loops

## Slide 8: Multicast Stitching with Per-VNI Load Balancing
PE nodes connected to multi-homed VXLAN network, perform BGP DF election to decide which PE node is responsible for forwarding multicast traffic associated with a given VNI.

## Slide 9: Next steps
Comments are appreciated.
Thank you