## Slide 1: draft-ietf-l2vpn-evpn-03.txt
A. Sajassi (Cisco), R. Aggarwal (Arktan), W. Henderickx (ALU), N. Bitar (Verizon), A. Issac (Bloomberg), J. Uttaro (ATT), F. Balus (ALU), R. Shekhar (Juniper), J. Drake (Juniper), S. Boutros (Cisco), K. Patel (Cisco), S. Salam (Cisco)
IETF 86, March 2013
Florida

## Slide 2: Changes from Rev02
Some changes in terminology
  Active/Active -> All-Active
  Active/Standby -> Single-Active
Added IANA allocations
Further clarifying ESI uniqueness requirement (6.0)
Further clarifying ES-Import RT (8.6)
Further clarifying Split-Horizon (9.3)

## Slide 3: Changes from Rev02 – Cont.
Describing Backup Path (9.4)
Added Route Resolution section (10.2.2)
Added “MAC Duplication Issues” (16.1)

## Slide 4: ESI Uniqueness (6.0)
ESI uniqueness is required for
  Auto-sensing and auto-deriving ES ID
  Auto-discovery of member PEs of an ES
  Aliasing
  Backup Path
If ESI uniqueness cannot be guaranteed from MHD or MHD protocols (e.g., LACP or MSTP), then it needs to be configured

## Slide 5: ES-Import RT (8.6)
Added text to describe ES Import Extended Community is of type RT
And thus a BGP speaker that implements RT-Constrain using RFC 4684, MUST apply RT-Constrain procedures to this RT.

## Slide 6: Split-Horizon (9.3)
Added a paragraph to further explain ESI label usage for split-horizon mechanism
  This label is only needed for All-Active mode of operation
  Furthermore, even with All-Active mode of operation, only non-DF PE MUST append this label for their BUM traffic – e.g., DF PE need not to send it.

## Slide 7: Backup Path (9.4)
Added a paragraph on the operation of Backup Path
  It is used for Single-Active mode for DHN (not MHN)
  PEs in an ES advertise Ether AD route with Active/standby flag set to 1 in the ext. comm.
  PEs in an ES also advertise Ether AD route per EVI for the same ESI
  Upon failure of the primary PE, remote PEs can switch to backup PE

## Slide 8: Route Resolution section (10.2.2)
If MAC route is for PBB-EVPN, then don’t wait for receiving Ether AD route (to do aliasing)
If MAC route is for a local ESI, then don’t alter forwarding state based on the received route
If MAC route is for a remote ESI, then only install forwarding state when both MAC route and Ether AD route (for that ESI) is received

## Slide 9: “MAC Duplication Issues” (16.1)
In case of mis-configuration where same host MAC address is configured on two different hosts, it is important to catch this scenario and avoid incrementing MAC mobility sequence no to infinity
A PE that detects MAC mobility event by way of local learning, starts a timer and if it receives N MAC moves within this time period, its must alert the operator and stop processing and sending MAC advertisement route for that MAC address

## Slide 10: Additional Changes for Rev04
More terminology
  EVPN instance as routing/forwarding table versus as VPN instance – need to define separate acronyms
Prefix length in MAC route (bits versus bytes)

## Slide 11: Next Step
Incorporate comments from IDR for BGP section
Publish Rev04
Initiate WG last call for Rev04