## Slide 1: draft-ietf-l2vpn-pbb-evpn-04.txt
Ali Sajassi (Cisco), Nabil Bitar (Verizon), Aldrin Issac (Bloomberg), Samer Salam (Cisco), Sami Boutros (Cisco), Florin Balus (ALU), Wim Henderickx (ALU), Clarence Filsfils (Cisco), Dennis Cai (Cisco), Lizhong Jin (ZTE)
March 2013
Florida

## Slide 2: Changes from Rev03
Minor edits: MES -> PEs
  (to be consistent with EVPN draft)
Several clarifications
  MAC route usage for PBB-EVPN
  Ether AD route
  MAC Mobility usage for PBB-EVPN

## Slide 3: MAC route usage for PBB-EVPN
Recall that there is no Ether AD route for PBB-EVPN
Recall that the same MAC route is used for EVPN and PBB-EVPN
Recall that both can coexist in the same PE
How does a PE differentiate between the two scenarios?
If ESI field is set to ESI-MAX, then this MAC route is for PBB-EVPN and the PE should not wait for Ether AD route to do aliasing
If ESI field is set to 0, then ES is single-homed

## Slide 4: Ether AD route Clarification
ESI values of 0 and MAX-ESI indicate that the receiving PE can resolve the path without an Ethernet A-D route

## Slide 5: MAC Mobility usage for PBB-EVPN
When MAC mobility extended community is used in PBB-EVPN, it indicates:
  C-MAC forwarding tables for the I-SIDs associated with the RT tagging the MAC Advertisement route must be flushed

## Slide 6: Next Steps
Draft has been fairly stable since March 2012
It is ready for WG last call