## Slide 1: LMAP BoF 1. ISP use case 2. Framework
Philip Eardley
BT
13 March 2013

## Slide 2: ISP use case
Identifying, isolating and fixing problems in the network
  Assist Test and Diagnostics tools
  Identify degradations as well as failures
  Identify issues affecting a group of customers (shared network element, equipment type, etc)
  Test network segments, as well as access line
  Scheduled and ad hoc tests needed
Design and planning
  To assist capacity planning & monitor suppliers
Understanding the impact and operation of new devices, technology, products and services
  IPv6, CGNAT, IPTV, new line cards…
Understanding the quality experienced by customers
  End-to-end service experience

## Slide 3: LMAP characteristics from ISP use case
Large-scale
  Capable of running tests on individual lines (panel is not enough)
  Potentially Measurement Agent in every edge and end device
Standardised
  Meaningful to compare measurements of same metric
  Allow operators to use multiple vendors for Measurement Agents
Diversity
  Measurement Agents in different devices (home hubs, set top boxes, edge devices), from different vendors, with different capabilities (wired, wireless)
On-demand tests
  By operator and by end user

## Slide 4: LMAP framework
Controller
Measurement Agent (MA)
Collector
Measurement Agent (MA)
Control protocol
Report protocol
test traffic
Measurement Agents
  Perform the test
Controller
  Manages MA (instructs what test to do & when; how to report results)
Collector
  Accepts results from MA

## Slide 5: Overall measurement framework
Controller
Collector
Measurement Agent (MA)
Measurement Agent (MA)
test traffic
IPPM
LMAP
LMAP should be open about what metrics are measured
  Use IPPM tests, referenced via the proposed IPPM registry
Control protocol
Report protocol

## Slide 6: Overall measurement framework
Controller
Collector
Measurement Agent (MA)
Measurement Agent (MA)
test traffic
Subscriber Parameter Database
Data Analysis Tools
Results database
IPPM
LMAP
LMAP should be open about use of measurement results
  After collection: used by ISP, regulator…
OAM
Control protocol
Report protocol

## Slide 7: Technical gaps (work for LMAP)
Define how the Controller instructs an MA about a test (Test /Report Schedule)
  What metric to measure (with what parameters), when, what conditions, how to report (where to and when).
Define how the MA reports results to the Collector (Report)
  What was measured, when, the actual results
… which requires …
Information model: abstract definition of Test /Report Schedule and of Report
  We want exactly one
Data model: instantiates the information model in a particular language.
  Eg JSON or YANG or (for the Report) IPFIX. Or non-IETF standard like XML.
Protocols: how to deliver the Test /Report Schedule and the Report.
  Eg NETCONF or a RESTful interface or (for the Report) IPFIX. Or a non-IETF protocol, like TR-69
  Reflect diversity of types of Measurement Agent

## Slide 8: Solution Constraints
To help meet the required characteristics
  especially large-scale
To simplify initial work whilst allowing future extensions

## Slide 9: Constraint #1: Measurement system under control of one organisation
Single organisation responsible for both data and user experience
Inter-organisation coordination is not precluded
  Interesting but raises additional issues (policy etc)

## Slide 10: Constraint #2: Measurement Agent has a single Controller at any one moment
Single Controller determines MA’s Schedule
  So MA does not have to manage contention between multiple, conflicting Schedules
  Simplifies MA design and deployment
Note, an operator may have several Controllers
  For different device types, scalability, resilience etc

## Slide 11: Constraint #3: Measurement Agent acts autonomously
MA operates tests and reports results without further reference to Controller (once it gets Schedule)
  Avoids frequent checks with Controller
  MA (on edge /end device) knows when not to run test due to user activity