## Slide 1: IPPM & LMAP: the glue
LMAP defines protocols
  between MA and controller to request tests
  between MA and collector to report test results
IPPM defines metrics for tests
The glue: a registry for metrics/tests so that the LMAP protocols can refer to a specific IPPM metric/test

## Slide 2: Protocol independent registry
Protocol Independent registry: Allows multiple protocols to be defined between Controller, Measurement Agents and Collector
  Within the same platform: e.g. IPFIX between the MA and the Collector and YANG/NETCONF between the Controller and MA
  Across different platforms: maybe some will use IETF protocols, others will use BBF TRxx protocols or else to request and report IPPM tests
  This may requires additional protocol specific fields in the registry

## Slide 3: What is in the registry?
New registry: tightly defined metric with few open parameters (don’t affect the nature of the test)
  e.g. source and dest address and the like
Less is more: reduced number of metrics proven useful
  Well defined metrics that have been proven useful in operations
Side benefits:
  Inventory of useful and used metrics
  Comparable test results even if performed by different implementations and in different networks

## Slide 4: Reference Path
Subsc Devic
Private Net 1
Private Net 2
Access Demarc
Intra IP Access
GRA GW
GRA GW
Transit GRA GW
Transit GRA GW
Access Demarc
Private Net n
Private Net n+1
Destination host
usually defined as the Ethernet interface on a residential gateway or modem
This is the first point in the access architecture beyond the Access Service Demarc. where a globally routable IP address is exposed and used for routing.

## Slide 5: Reference Path
Subsc Devic
Private Net 1
Private Net 2
Access Demarc
Intra IP Access
GRA GW
GRA GW
Transit GRA GW
Transit GRA GW
Access Demarc
Private Net n
Private Net n+1
Destination host
mp000
mp100
mp150
mp190
mp200
mp800
mp890
mp900