## Slide 1: MPLS Special Purpose Labels
draft-kompella-mpls-special-purpose-labels-01
Loa Andersson
Adrian Farrel
Kireeti Kompella

## Slide 2: Two Things
Making the new name “special purpose labels” official, and listing relevant RFCs
What about extended special purpose labels in the range 0-15?

## Slide 3: A Rose by any other Name (would smell as special)
Renaming “reserved” labels to “special purpose” labels
  IANA uses “reserved” in a different way
  Many RFCs use the term “reserved” labels
  State that this doc updates those RFCs
  May help reduce confusion and maybe help evangelize the new term
Loa has gone through this exercise
  Renaming of “EXP field” to “TC field”

## Slide 4: Extra Special Special Purpose Labels
Some reserved^H^H^H^H^H^H^H^H special purpose labels have meanings independent of where they are in the stack
  For others, it may be convenient to assume this to avoid breaking existing implementations or to simplify implementations
Labels to consider here: ELI, RA, GAL, OAM, Explicit Null

## Slide 5: Extra Special Special Purpose Labels
The Entropy Label Indicator (ELI) label (7) may occur anywhere in the stack
  RFC 6790 says one may search through the stack looking for this label, and use the next label as the Entropy label (to use for load balancing)
  Doesn’t say anything about being after label 15!
The ELI MUST retain its meaning independent of whether or not the preceding label is the extension label (15)

## Slide 6: Extra Special Special Purpose Labels
RFC 4182 effectively states that Explicit Null labels (0, 3) may occur anywhere in the stack
  Used to be legal only at bottom-of-stack
If an explicit null label bubbles to the top of stack, it should be popped
Should explicit labels retain their meaning even if they occur after the extension label?
  In theory, not necessary
  In practice, need to look at implementations

## Slide 7: Extra Special Special Purpose Labels
GAL label (RFC 5586)
  “Upon reception of the labeled packet, the targeted destination, after having checked both the LSP Label and GAL LSEs fields, SHOULD pass the whole packet to the appropriate processing entity.“
OAM label (RFC 3429)
Do current implementations look through the label stack searching for the GAL/OAM label?

## Slide 8: Extra Special Special Purpose Labels
Router Alert labels
  Do current implementations look through the label stack searching for the RA label?
  Or only act on it them when they bubble to the top of stack?

## Slide 9: Proposed Solution
When the extended label is defined, pre-reserve some of the non-extended special purpose labels
  State that they retain their meaning even as extended special purpose labels
  State that label 15 is not legal after label 15
When a new non-extended special purpose label (0-15) is defined, check if necessary to pre-reserve same value in the extended space

## Slide 10: Publish it already?
Or maybe make it a WG doc first?