## Slide 1: Ravi Singh (ravis@juniper.net) Yimin Shen (yshen@juniper.net) John Drake (jdrake@juniper.net)
IETF-86 (Orlando)
speaker: Ravi Singh
draft-ravisingh-mpls-el-for-seamless-mpls-00
Entropy Label for Seamless MPLS

## Slide 2: Entropy label: Summary (from RFC-6790)
  RFC-6790 defines EL usage for
    Single-segment LSPs
  Router roles:
    Ingress LER: label-inserting-router computes and PUSHes the (ELI+EL) before PUSHing the transport-LSP label
      Based on egress signaling its ability to POP (ELI+EL)
    (Egress LER)/PHR: removes the (ELI+EL) after POPing transport-LSP label
    Transit router: utilizes presence of the ELI to hash solely on the EL/label-stack to pick outgoing link of ECMP/LAG
  Use of (ELI+EL) reduces maximum-payload of the LSP by 8 bytes

## Slide 3: Terminology:
  Intrinsically-EL capable/capability (ELC): An LSP (segment or e2e) is (or has) ELC: when…
    ingress LER of (segment or e2e) LSP: has ability as specified by RFC-6790
    egress/PHR of the (segment or e2e) LSP: has ability as specified by RFC-6790
  Notional ingress/egress LER: Ingress/egress LER (usually a stitching point) for an LSP segment that is respectively PUSHing/POPing the (ELI+EL) on traffic going over an e2e LSP
  Notional LSP segment: portion of the e2e LSP between a consecutive notional ingress and notional egress LER. An e2e LSP might have more than 1 such.

## Slide 4: Entropy label & Seamless MPLS: 1/2
  Seamless MPLS:
    Deploy MPLS in access/aggregation networks
    By setting up e2e LSPs
  E2e LSPs rely on:
    LSP stitching
    LSP hierarchy
  On an e2e LSP:
    LAG/ECMP might appear anywhere between the ultimate ingress and ultimate egress
    Routers on path from ultimate ingress to ultimate egress will have varying hash computation capabilities

## Slide 5: Entropy label & Seamless MPLS: 2/2
  Aim: Get load-balancing benefits of EL wherever possible
  How to get load-balancing benefits…
    when the e2e LSPs may not be intrinsically ELC?
    when a transit router’s forwarding ASICs not able to include an EL (past a certain depth in the label stack) for hashing?
    without unnecessarily reducing the payload capacity of the e2e LSP?
  This draft: extends/optimizes EL definition for LSP stitching and LSP hierarchies. Specifies…
    rules of ELC propagation at stitching points;
    data-plane guidelines at the stitching point; and
    the data/mgt-plane guidelines for LSP hierarchies for inserting (ELI+EL) at ingress LER.

## Slide 6: LSP stitching: Problems / requirements 1/2
  LSP stitching point involves:
    Incoming LSP segment: Li
    Outgoing LSP segment: Lo
    A stitching point router that is connecting Li and Lo
S
A
B
C
D
L1
L3
L4
e2e LSP is made of LSP segments L1, L2, L3 and L4.

## Slide 7: LSP stitching: Problems / requirements 2/2
  Problem: How to…
    get load-balancing benefits even though an e2e LSP may not be intrinsically ELC?
      How to get EL benefits even though the e2e LSP may not support ELC from end to end?
    not run into data plane issues due to EL insertion?
  Requirements: Modes to be supported:
    Per-segment ELC
    ELC for notional segment LSP(s)
    ELC for e2e LSP

## Slide 8: LSP hierarchy: Problems / requirements 1/2
  Problems: How to…
    prevent unnecessary reduction of max-payload of the LSP by EL?
    prevent possibility of EL being unusable?
A
B
C
D
E
D1
S2
LSP1: B->D (Yellow LSP)
LSP2: A->E, tunneled through LSP1 (Green LSP)
LSP3: S1>D1 , tunneled through LSP2 (Red LSP)
LSP4: S2->D2, tunneled through LSP2 (Black LSP)
All of the above LSPs are ELC
D2
S1

## Slide 9: LSP hierarchy: Problems / requirements 2/2
  Requirements:
    Insert only 1 (ELI+EL) on a data packet
    Flexibility in choice of LSP tunnel for which EL is inserted

## Slide 10: LSP stitching: New abstractions 1/3
  Additional router roles:
    Notional ingress: the segment ingress that is inserting (ELI+EL). Could be different from e2e LSP ingress.
    Notional egress: the segment egress that is POPing (ELI+EL). Could be different from e2e LSP egress.
  Possibility of multiple notional ingresses and notional egresses on an e2e LSP.
    1 notional ingress per notional egress
    Notional ingress and notional egress alternate
  EL lifetime on a packet:
    Between a notional ingress and a notional egress

## Slide 11: LSP stitching: New abstractions 2/3
  SIGNALING: ELC translation rules at stitching point: translating ELC from Lo to Li
  As segment egress…
    signals ELC…
      when this egress segment is intrinsically ELC for Li, or
      when segment Li is not intrinsically ELC, but segment egress for segment Lo is ELC.
    MUST NOT signal ELC when…
      Lo’s segment egress is not signaling ELC, and
      this router does not have ability to POP (ELI+EL) on Li.
  As segment ingress:
    Bidir LSPs: When this router is signaling ELC on Li, must also signal ELC for Lo

## Slide 12: LSP stitching: New abstractions 3/3
  FORWARDING: Data plane rules to be implemented:
  Handling differing EL dispositions at stitching point:
    Notional egress/ingress behavior: Differing (Li, Lo) ELC will result in insertion/removal of (ELI+EL) for traffic going into Lo for following (Li, Lo) ELC cases-space :
      {(no-ELC, ELC), (ELC, no-ELC)}
    Implicit notional ingress behavior: when (Li, Lo) ELC is (ELC, ELC), this router will insert (ELI+EL) if incoming data packet does not have (ELI+EL)
  Preventing multiple (ELI+EL) on a packet: insert (ELI+EL) only if incoming packet does not already contain an (ELI+EL)
  Dealing with role changes due to configuration
    “Notional ingress -> Not a notional-ingress”, or vice versa
    “Notional egress -> Not a notional egress”, or vice versa

## Slide 13: LSP Hierarchy: New abstractions
  Ensuring EL stays usable for load-balancing:
  Management plane triggered data plane changes:
    Allow disabling insertion of (ELI+EL) on a per LSP basis
    Allow tweaking of the LSP in the hierarchy that ends up with an (ELI+EL) inserted
  Preventing multiple ELs getting imposed on a data packet:
  A router MUST NOT insert an (ELI+EL) on a data packet that already contains an ELI

## Slide 14: Next steps
  Discussion on the MPLS WG mailing list
  Moving the draft towards acceptance as a WG document