## Slide 1: Conditional Enablement
draft-kwatsen-conditional-enablement-00

## Slide 2: Disclosure
This preso now goes past enablement
It’s now includes assignment and triggers too…

## Slide 3: Motivation
Ad-hoc nodes defined in various drafts
  Static Disablement
    enabled, use-ntp, enable-nacm, etc.
Use in JUNOS and Tail-F’s products
  Static Disablement
    XML Attribute “inactive”
  Temporal Configuration
    “when” conditions in Configuration Group definitions
I2RS Requirements
  Temporal Configuration
    Enabled at start-time with optional expiration-time or duration
  Triggered Configuration
    Enabled based on asynchronous events with optional duration

## Slide 4: Use Cases
End-user wants to manually disable a part of the configuration without losing it forever
End-user wants a part of the configuration to automatically become active based on time or an async event
End-user wants a part of the configuration to automatically become inactive based on time or duration

## Slide 5: Strategies Discussed on List
Concern for XML attributes
  YANG doesn’t model (but XSD or RelaxNG could be used)
  Not referenceable via must/when statements (really?)
Standardize an “enable” or “disable” leaf
  e.g. 6021bis (ietf-yang-types)
Use Xpath just for complex expressions
  Can’t do time-of-day
  Not easy for a NMS to import
Use a rulebase like NACM
Implement conditional config like a 1st-class “patch” object

## Slide 6: Other Considerations
Client discretion vs. modeler’s selection
Flags need to be available to must/when statements and XPath select in get operations
Access to the rule-base that controls the enable property for object X is different than access to object X directly
Validation should conceptually after disabled nodes have been filtered out
Should running config include conditional policy or just its evaluation?

## Slide 7: Updated Proposal
Use XML attributes for static/const “disable” flag
  Simple
  We allow XML attributes for metadata
  Client can disable any arbitrary subtree
  No impact to must/when statements
  Assume disabled node are removed prior to validation
Introduce a mechanism for temporal/triggered
  Modeled within config or external (e.g. cron)???
  JUNOS has temporal setting within the config
    Like a template – a complete tree
    Next slide illustrates idea

## Slide 8: Temporal/Triggered Configuration
Operational Configuration
Running/Candidate Configuration
Root
Unconditional Configuration
Top-Level Tag
Condition-1 Configuration
Condition-N Configuration
If recv(interface-down event)
If (M-F 9-5)
strip out disabled nodes
and validate against YANG

## Slide 9: Next Steps
Take on as a chartered working group item?