## Slide 1: Network Virtualization Hypervisor-to-NVE Control Protocol Requirements
draft-kreeger-nvo3-hypervisor-nve-cp-01
Lawrence Kreeger, Thomas Narten, David Black

## Slide 2: Terminology
Need a better term for “oracle”. We are using IMA for “Information Mapping Authority”
VNIC: A Virtual NIC that connects a Tenant System to a Virtual Network Instance (VNI).
Rename VNIC to Tenant System Interface (TSI)?

## Slide 3: VNIC / Address Association
VNIC connects to a Virtual Network with a MAC and (optionally) an IP address
VNIC--VN--MAC—IP
VNICs migrate along with the VMs they are part of

## Slide 4: VNIC / Address - complex case
VNIC connects to multiple Virtual Networks with multiple MACs and IP addresses
VNIC-+-VN-+-MAC-+-IP
| | +-IP ...
| |
| +-MAC-+-IP
| +-IP ...
|
+-VN-+-MAC-+-IP
| +-IP ...
|
+-MAC-+-IP
+-IP ...
Signaling of VNIC migration (versus shutdown/startup) can help the NVE when a VNIC with a complex containment structure exists

## Slide 5: Next Steps
  draft-kreeger-nvo3-hypervisor-nve-cp-01
    Authors met with some authors of related drafts draft-gu-nvo3-tes-nve-mechanism and draft-kompella-nvo3-server2nve-01
    Plan: Include VM lifecycle events to motivate detailed requirements
    Will ask that resulting draft be adopted as WG draft
Adopt as Working Group draft the NVE to oracle (IMA) control plane requirements
  draft-kreeger-nvo3-overlay-cp-req-02