## Slide 1: Security Requirements of NVO3
draft-hartman-nvo3-security-requirements-00
Sam Hartman, Dacheng Zhang, Margaret Wasserman
IETF 86, March. 2013, Orlando, USA
Notes: 1

## Slide 2: Introduction
  Propose a threat model in order to specify the attacks of concern
Analyze the security requirements that the control plane and the data plane MUST or MAY fulfill in order to tolerate the attacks concerned

## Slide 3: Threat Model (1)
NOV3 should be secure even when an attacker has the capability of
  Intercepting the packets transported through a virtual data center network
  Replaying the intercepted packets
  Generating fake packets and injecting them into the network
When using the above capability to perform a successful attack on a virtual data center network, an attacker may be able to
  Obtain the data which it is un-authorized to access
  Analyze the traffic pattern of a tenant or a end device
  Disrupt the service quality of the network or the integrity of application running over the network

## Slide 4: Threat Model (2)
Under the attacks performed by an attacker, a virtual data center network MUST guarantee the following security properties
  Isolation of virtual networks
  The traffic within a virtual network can only be transited into another one in a controlled fashion
  An entity cannot make use of its privilege obtained within a VN to manipulate the overlay control plane to affect on the operations of other VNs
  Integrity and origin authentication of the control plane: All the control pane implementations of the overlay MUST support the integrity protection on the signaling packets.
  Availability of the control plane: The design of the control plan must consider the DDOS or DOS attacks.

## Slide 5: Threat Model (3)
The following properties SHOULD be optionally provided:
  Confidentiality and integrity of the TES traffic
  If most of the TES data is headed towards the Internet and nothing is confidential, encryption is redundant
  in the cases where the underlay network is secure enough, no additional cryptographic protection needs to be provided
  Confidentiality of the control plane.
  On many occasions, the signaling messages can be transported in plaintext
  When some information contained within the signaling messages are sensitive to a tenant (e.g., the location of a TES, when a TES migration happens), the signaling messages related with that tenant should be encrypted.

## Slide 6: Security Requirements Between NVEs and TESes
When a NVE and the TESes it supports can be deployed in a distributed way:
  Optional security protection on the data traffic
  Integrity of signaling messages: Mutual Authentication needs to be provided
  Isolation between different VNs: data traffic and signaling messages (Authorization is required)
When a NVE and the TESes it supports can be deployed in a co-located way:
  Isolation between different VNs
  Isolation of Memory and Computing Resources

## Slide 7: Security Requirements within Overlays -Control Plane
The integrity and origin authentication of the signaling messages must be guaranteed
DOS attacks
  The NVEs SHOULD be only allowed to send signaling message in the overlay with a limited frequency
  Protection on the centralized servers
Inside attacks where one or more NVEs are compromised
  Authentication and authorization
  Isolation enforced with cryptographic keys

## Slide 8: Security Issues Imposed by the New Overlay Design Characteristics
Scalability
  If a NVE needs to securely communicate with a large number of peers, the scalability issue could be serious.
  In[I-D.ietf-ipsecme-ad-vpn-problem], it has been demonstrated it is not trivial to enabling a large number of systems to communicate directly using IPsec to protect the traffic between them.
Influence introduced by data encryption on Security Devices
Security Issues with VM Migration
  State Migration
  Redirection

## Slide 9: Questions?