## Slide 1: IP/MPLS VPN Protocol GAP Analysis For NVO3 draft-hy-nvo3-vpn-protocol-gap-analysis-02
Lucy Yong Susan Hares
March 2013 Orlando FL

## Slide 2: About this Draft
Analyze IP MPLS L2/L3VPN protocol applicability and gaps for NVO3
Intend to stay at neutral regarding
  Should extend and/or simplify the VPN protocols or
  Develop a new protocol solution for NVO3
The document is organized:
  IP/MPLS L2/L3 VPN Highlight
  L2/L3 VPN for NVO3
  L2/L3 VPN for DCI when NVO3 is used
  Operator Aspects

## Slide 3: NVO3 Requirements
Many NVOs are built on a common infrastructure with:
  Traffic isolation among one another
  Independent address space in each and isolated from infrastructure’s
  Flexible VM placement and move from one server to another without physical network limitation (no change on VM addresses when move)
  No Communication b/w an end system in an overlay and a transport underlay
  Scalability and security support
An NVO may be L2 or L3 based where:
  The Tenant System (TS) may be VM or Server
  Network Virtual Edge (NVE ) may be on Server or ToR
  Server may run as a host or a network overlay edge in DC underlying network
Interwork with other NVO instances
Allow external user to access an NVO
NVE
NVE
TS
TS
TS
TS
Tunnel
NVO3 Model
VM
VM
UN
VM
VM
VM
DC Site
VM
NVO1
NVO2

## Slide 4: Quick Comparison
Assumption: TS <-> CE, NVE <-> PE , Tunnel b/w NVEs <-> Tunnel b/w PEs
Notation: Support ( √ ), May Support (≤) , Not Support(×) , Not Apply (≠)
NVO3 Requirements | VPN | Clarification
Traffic Isolation | √ | 
Own Address Space | √ | 
Be L2 or L3 based | √ | 
Decouple from underlying transport | √ | VPN traffic is decoupled from underlay transport
VM Mobility | × | support cold move in L2VPN, but not hot move
Flexible VM placement operation | ≠ | host placement is at CE site, VPN has no visibility to it
NVE on ToR | √ | when ToR supports VPN PE function
TS and NVE on a Server | ≠ | PE and CE are physically separated
VM as Tenant System | ≤ | via hypervisor
Server as Tenant System | √ | like CE as a host
NVE is on a server that is a host in UN | ≠ | use tunnel? need /32 host routing
VNI Table | ≤ | support well if NVE is on ToR, may not if NVE on Server
Reachbility advertisement | √ | Via control/data plane protocol, or static configuration
Tunneling | ≤ | VPN uses MPLS LSP Tunnel, rarely others

## Slide 5: Quick Comparison Cont.
NVO3 Requirements | VPN | Clarification
Auto discovery | √ | NVE discovery
Load Balancing | ≤ | ECMP function in WAN may not be sufficient for NVO3
Broadcast or Multicast | √ | May not good enough
Underlying Network Design | ≤ | DC network design may or may not be same as WAN’s
Gateway | ≤ | L3VPN GW may not be sufficient for NVO3, L2VPN has no
Multi data plane interworking | × | Only support one data plane schema
Inter ASs | ×, √ | L3VPN support, not L2VPN
NVO Access externally | ×, √ | L2VPN does not have it, L3VPN supports extranet access
Scalability | ≤ | Depend on the configuration, i.e. NVE is on ToR or on server.
Operation Aspect | × | DC operation model may be very different from SP model
SDN controller management | x | this is new to VPN
Notation: Support ( √ ), May Support (≤) , Not Support(×) , Not Apply (≠)
Clearly, commons and gaps exist between IP/MPLS VPN and NVO3 requirements Sum: √ (11), ≤ (7), × (6), ≠ (3)

## Slide 6: VPN Interconnect DC Underlay Networks
IP/MPLS VPN interconnects DC underlay networks
  VPN does not have the visibility of any network virtual overlays
  PE connects to DCGW (as CE) via a local interface or sub-interface
  PE may run OSPF, eBGP, etc, DCGW peers with PE only, not remote GW
An NVO span across DC sites w/o PE/DCGW awareness
  Overlay tunnels are built between any pair of NVEs directly
  NVO control plane runs independently from WAN VPN control plane
VPN for NVO and VPN for DCI are orthogonal in this case
VM
UN
VM
DCGW
VM
DC Site A
VM
NVO1
NVO2
VM
VM
PE
VM
VM
UN
VM
VM
DC Site B
VM
NVO1
NVO3
DCGW
PE
IP/MPLS
VPN

## Slide 7
DC NVO Access via a WAN VPN
DC NVO may be accessed via an IP/MPLS VPN
  VPN connects to both DC NVO and Enterprise sites
    PE may peer with Enterprise sites
    VPN CP needs to interwork with NVO CP and Enterprise CP
  An NVO GW entity is necessary on the DCGW
    Be the member of DC NVO and terminate NVO tunnels
    May perform routing, NAT, policy, firewall functions
  PE may perform some gateway function too
DCGW may be configured with many NVO GW entities for diff. customers
If NVO uses VPN solution, this will be like inter-AS scenario in RFC4364
This may require VPN enhancement
  Interwork with NVO Control Plane, support VM mobility, optimize traffic path, etc
DC Site A
WAN
VM
VM
NVO
DCGW
IP/MPLS
VPN
PE
VM
VM
VM
PE
PE
NVO
VM
VM
VM
VM
DC Site B
DCGW
Enterprise Site 1
Enterprise Site 2
CE
CE

## Slide 8: Next Step
Welcome comments and suggestions
Ask chair suggestion for the next
  draft-hy-nvo3-vpn-protocol-gap-analysis-02