## Slide 1
Network Coding Overview
NWRC meeting
March 11, 2013

## Slide 2: Coding  Network Coding
Coding Today
(all end-to-end)
Coding Tomorrow
(using Random Linear Network Coding)
Classical
Network
Multipath
Multisource – Multi-destination / Mesh
Multicast

## Slide 3: Why RNLC is Different
Code Capabilities | RLNC | Rateless (e.g. Fountain) Codes | Block Codes
Erasure correction | ✔ | ✔ | ✔
Code is carried within each packet | ✔ | ✗ | ✗
Completely distributed operation | ✔ | ✗ | ✗
De-code using unencoded packets | ✔ | ✗ | ✗
Able to generate valid codes from coded or unencoded packets | ✔ | ✗ | ✗
Composability without decoding (add incremental redundancy) | ✔ | ✗ | ✗
Encode data in a sliding window | ✔ | ✗ | ✗

## Slide 4: Initial RLNC Stack Implementations
Application Layer
Physical Layer
Network Layer
IP Layer
UDP
TCP
RLNC
RLNC
TCP Socket
RLNC
RLNC
RLNC
RLNC
Operating System Agnostic Implementation
(Software)
Chip
Implementation
(Hardware)
Kernel
Implementation
(Software)
Implementable at any layer as a patch

## Slide 5: Application Layer TCP Case Study
Multisource – Multi-destination
Classical
Multipath
Network
Application Layer
Physical Layer
Network Layer
IP Layer
UDP
TCP
RLNC
RLNC
RLNC
RLNC
RLNC
RLNC
TCP Socket

## Slide 6: TCP Ill-Suited to Random Losses
TCP
sender window
p1 p2 p3 p4
p1
p2
p3
ACK(p1)
ACK(p1)
p2 p3 p4 p5
p5
ACK(p1)
Can’t increment window by 1
Partial sliding window
Triple-duplicate ACKs!
p2 p3
p4
Window closing: W ← W/2
ACK(p1)

## Slide 7: Coded TCP Maintains Throughput
Coded TCP
sender window
p1 p2 p3 p4
Σp
SEEN(1)
SEEN(2)
p4 p5 p6 p7
SEEN(4)
SEEN(5)
SEEN(6)
Σp
Σp
Σp
Σp
Σp
Prevents random losses being interpreted as congestion!
Σp
SEEN(3)
p7 p8 p9 p10 p11
There is a lag in the “SEEN” acks: To avoid lag, introduce redundancy!
SEEN(7)
Σp
p8 p9 p10 p11 p12
Minij Kim, Muriel Médard, João Barros
Modeling network coded TCP throughput: a simple
model and its validation
Valuetools, 131-140 (2010)

## Slide 8: Performance With Congestion Losses
TCP
TCP/NC
sender window
sender window
p1 p2 p3 p4
p1 p2 p3 p4
p1
p2
p3
ACK(p1)
p2 p3 p4 p5
Σp
SEEN(1)
Σp
Σp
Still allows congestion control while masking random losses!
Time-out!
p2
p4
Window closing: W ← 1
Σp
p2 p3 p4 p5
Time-out!
p2
Window closing: W ← 1
Waiting…
Waiting…

## Slide 9: Experimental Results: Single Path
Server: Amazon EC2 instance in CA
Client: Desktop at RLE MIT, using WiFi(s)
wlan0
Loss rate | 0% | 1% | 2% | 3% | 4% | 5%
TCP (Mbps) | 19.04 | 3.07 | 1.07 | 0.82 | 0.53 | 0.47
CTCP (Mbps) | 20.40 | 18.99 | 16.52 | 15.20 | 13.46 | 13.53
> 100 ms
Chart: Loss Rate
| 0.0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05
Coded TCP | 20.4 | 18.99 | 16.52 | 15.2 | 13.46 | 13.53
TCP | 19.04 | 3.07 | 1.07 | 0.82 | 0.53 | 0.47
Coded TCP
TCP
130 seconds to transmit
6 seconds to transmit
Leo Urbina
Applying Network Coding to TCP
MIT M.Eng. Thesis 2012

## Slide 10: Experimental Results: Single Path
Example: 2% loss
Average Throughput: 0.77 Mbps
Average Throughput: 15.29 Mbps

## Slide 11
Testbed Measurements
60 s video
Full download
60 s video
Progressive download
Minji Kim, Jason Cloud, Ali ParandehGheibi, Leonardo Urbina, Kerim Fouli, Douglas Leith, Muriel Médard
Network Coded TCP (CTCP) arXiv: 1212.2291v2

## Slide 12: WiMax Experiments
Notes: Rountrip time variability

## Slide 13: Coded TCP Network Improvements
Multisource – Multi-destination
Classical
Application Layer
Physical Layer
Network Layer
IP Layer
UDP
TCP
RLNC
RLNC
RLNC
RLNC
RLNC
TCP Socket
Multipath
Network
RLNC

## Slide 14: Coded TCP (CTCP) Over a Network
Longer paths lead to higher losses, resulting in poor performance
  TCP’s performance degrades super-linearly with end-to-end loss rate  benefits of Coded TCP are even greater in this scenario
10% loss
source
client
10% loss
10% loss
10% loss
 | RLNC (using Coded TCP) | End-to-End Coding (including Fountain Codes)
Best Possible Throughput Rate | 0.9 | 0.66
Notes: If p1 is the probability of success in link 1 (and so on) why is effective success rate (1-p1)(1-p2)… and not p1*p2… ?

## Slide 15: Composability: Redundancy When Needed
Randomized Distributed Network Coding
20% Loss Node
Over reliable network send minimum packets
(4 variables, 4 packets)
8 P1+ 6 P2+ P3+ P4
7 P1+2 P2+3 P3+4 P4
P1+ P2+ 4 P3+ 2 P4
2 P1+ 8 P2+ 9 P3+P2
RLNC allows optimized packet sends at any node
Re-encode  add a packet without de-coding
(4 variables, 5 packets)
3P1+ 5P2+ 2P3+ 7P4
Needed packets arrive
(4 variables, 4 packets)
8 P1+ 6 P2+ P3+ P4
7 P1+2 P2+3 P3+4 P4
2 P1+ 8 P2+ 9 P3+P2
3P1+ 5P2+ 2P3+ 7P4
8 P1+ 6 P2+ P3+ P4
7 P1+2 P2+3 P3+4 P4
P1+ P2+4 P3+ 2 P4
2 P1+ 8 P2+ 9 P3+P2

## Slide 16: Coding Coefficients Carried within Packet
Jay Kumar Sundararajan, Devavrat Shah, Muriel Médard, Szymon Jakubczak, Michael Mitzenmacher, João Barros,
Network Coding Meets TCP: Theory and Implementation. Proceedings of the IEEE 99 (3): 490-512 (2011)

## Slide 17
1
2
4
3
FTP
sender
From given data
FTP
receiver
Multihop Wireless Network

## Slide 18
TCP | End-to-end coding | Re-encoding at node 3 only
0.0042 Mbps | 0.1420 Mbps | 0.2448 Mbps
(assuming each link has a bandwidth of 1 Mbps in the absence of erasures)
Time average throughput (over 641 seconds)
Performance Comparison

## Slide 19: CTCP versus Multipath TCP Using Routing
MPTCP may potentially provide multi-path communication BUT:
  Difficult and complex scheduling at the source needed
  Round-robin scheduling is inefficient
10% loss on each link
source
client
-10%
-10%
-10%
-10%
-10%
-10%
-10%
-10%
-10%
-10%
-10%
-10%
-10%
CTCP provides multi-path communication throughput of 2.7 without complex scheduling at the source
Notes: If p1 is the probability of success in link 1 (and so on) why is effective success rate (1-p1)(1-p2)… and not p1*p2… ?

## Slide 20: Experimental Results: Multiple Path
Server: Amazon EC2 instance in CA
Client: Desktop at RLE MIT, using WiFi(s)
Limited each path to < 8-9 Mbps
wlan0
Loss rate | 0% | 1% | 2% | 3% | 4% | 5%
wlan0 (Mbps) | 7.13 | 6.08 | 6.43 | 6.25 | 5.16 | 5.08
wlan1 (Mbps) | 7.11 | 5.92 | 6.53 | 5.90 | 5.01 | 4.58
CTCP (Mbps) | 14.23 | 12.03 | 13.08 | 11.88 | 10.10 | 9.34
wlan1
> 100 ms
Example:
0% loss
Combined throughput at Client
Throughput on wlan0

## Slide 21: Application Layer Base Station Case Study
Multisource – Multi-destination
Multipath
Application Layer
Physical Layer
Network Layer
IP Layer
UDP
TCP
RLNC
RLNC
RLNC
RLNC
RLNC
RLNC
TCP Socket
Classical
Network

## Slide 22
Value of Goodput with User Growth
Problem Statement: As # of users grows, additional base stations are added for throughput, not coverage
RLNC improved goodput = fewer Base Stations
MinJi Kim Thierry Klein Emina Soljanin João Barros Muriel Médard
Modeling Network Coded TCP: Analysis of Throughput and Energy Cost
http://arxiv.org/abs/1208.3212 2012 CoRR abs/1208.3212 db/journals/corr/corr1208.html#abs-1208-3212

## Slide 23
RLNC Expands Base Station Reach
5.08 MB
Increasing
User
Activity
Joint research with MIT and Alcatel-Lucent
# of Base Stations
With RLNC operators lower both OpEx and CapEx

## Slide 24: Link Layer Implementation Case Study
Multisource – Multi-destination
Classical
Multipath
Network
Application Layer
Physical Layer
Network Layer
IP Layer
UDP
TCP
RLNC
RLNC
TCP Socket
RLNC
RLNC
RLNC
RLNC

## Slide 25
Network Coding vs. ARQ and HARQ
Scenario: 5-packet block transfer from BS to SS
Downlink: fixed 40% packet error pattern (every 3rd and 5th packet)
Uplink: feedback NACKs not subject to loss
ARQ: repeated transmissions create RTT feedback loops
HARQ: feedback reduced by combining corrupted packet versions
Network Coding: a-priori systematic coding with added redundancy of 3/5
Clear delay, throughput, and energy gains
  No feedback loop
  Redundancy cost amortized over block
Surat Teerapittayanon, Kerim Fouli, Muriel Médard, Marie-José Montpetit, Xiaomeng Shi, Ivan Seskar, Abhimanyu Gosain
Network Coding as a WIMAX Link Reliability Mechanism
MACOM 2012L 1-12
Surat Teerapittayanon, Kerim Fouli, Muriel Médard, Marie-José Montpetit, Xiaomeng Shi, Ivan Seskar, Abhimanyu Gosain
Network Coding as a WIMAX Link Reliability Mechanism: An Experimental Demonstration
MACOM 2012: 75-78

## Slide 26
Experimental Setup
Intra-flow NC modules at the Base Station (BS) and Subscriber Station (SS)
Toggle ARQ, HARQ, and various NC configurations
IPERF  application-layer throughput / loss
UFTP (FTP over UDP)  application-layer file-transfer delay

## Slide 27
IP-Based Implementation
WiMAX MAC inaccessible  IP-based implementation
Performance measurements at the application layer (IPERF and UFTP)
IP layer: Netfilter used to intercept packets, route them to encoder/decoder, then re-inject them to IP layer
PDCP does not need to be involved, although that may be quite doable
Network coding included at the e-Node B before handing it to the MAC, and ARQ and HARQ bypassed at the MAC – does not require a proxy, but can be used if convenient. Occurs below transport, so not touching TCP per se
Remote access of eNode B
Card driver

## Slide 28
Consistency
Loss
Throughput
File transfer delay
NC-Best decreases packet loss from 11-32% to nearly 0%
NC offers up to 5.9x gain in throughput and 5.5x reduction in file transfer delay

## Slide 29
Looking Forward
The applications of network coding are varied and changing
This is indeed the right time for a standardization effort
Network coding can be implemented at different layers and in different portions of the network
Standardization should allow the flexibility needed to allow these diverse implementations