## Slide 1: CONCERTO and BRAVO Experiences with practical, full implementations of Network Coding systems
Victor Firoiu 11 March 2013

## Slide 2: Projects in Networking and Communications
2006
2007
2008
2009
2010
2011
DARPA CBMANET/ CONCERTO
ONR Adaptive Networks/ BRAVO
DARPA IAMANET/ PIANO
DARPA SAFER/ SONATA
Network Coding system for MANETs
Secure Network Coding
2012
2013
BRAVO NG
Anonymous Comms
through Net Coding
Network Coding using local info, high mobility

## Slide 3: CBMANET/ CONCERTO Motivation
Challenges in Wireless MANETs
Wireless communication
  MANET Broadcast transmissions – use Rx is better than ignore
  Reception is prone to errors – needs as much help as can get
Mobility removes certainty from traditional routing
CONCERTO Approach
Clean slate network and transport layers
Network Coding Transport: fluid model
Routing on Subgraphs
  Enabled by fluid model
  Robust to link errors and topo change

## Slide 4: Subgraph Computation
Optimal Subgraph computation is complex (exponential in no. neighbors)
Simplified approach: similar to MORE by Katabi et al
  Requires Link State information
  Computational complexity is O(n2) (n nodes in network)
  Computes rate at which nodes should participate in forwarding mixtures
Basic Concept
  Forwarding nodes are chosen from those that are most probable to advance the information propagation to each destination
  Forwarding intensity is related to the probability of contributing to info advance
D
S
Can contribute significantly
to info advance to D
Can not contribute
significantly
to info advance to D
Rij
Forwarding intensity:
Assigned Information rate

## Slide 5: Packet Forwarding
Packet Forwarding
  Uses transmit rates computed by
  Subgraph computation
  Computes “receive credit” as ratio of transmit rate to expected receive rate
  Node earns credit when it receives innov. packet
  Spends credit when it transmits packets
  Provides automatic scaling to source rate
Repair process, semi-reliable protocol (media streaming)
  Nodes request locally extra transmissions if necessary
  Requests are piggy-backed on forwarded packets when possible
Fully reliable protocol (file transfer)
  Additional algorithm for propagation of repair requests, detection of missing generations, beginning/end of files, late join, etc.

## Slide 6: CONCERTO Architecture
Group
Def
Group Cache
Neighbor Discovery
PIM
Module
Net Coder
SG
Constructor
Master Fwder
Topology
Ethernet
SG Def
Role
NC Pkt Window
Gen Mgr
Fwdr
NC
Buf
NC Pkt Window
Gen Mgr
Fwdr
NC
Buf
Rank Feedback
Topo Cache
Topo Info
Topo Info
Nbr Info
NC Pkt Window
Gen Mgr
Fwdr
NC
Buf
NC Pkt Window
Gen Mgr
Fwdr
NC
Buf
TransmitModule (Simple)
IGMP
Serialization
Data Marshaller
Neighbor Discovery
IGMP
Module
PIM
App
OLSR
PIM
AppIF
Group Def
802.11
PhyRadio (UDP)
Multipath
“Subgraph”
Routing
Network Coding Engine
(intra-session)
Network Coding Forwarder
Layerless Modular Architecture: module info sharing  Adaptation to wireless dynamics

## Slide 7: Scenario
7
31 mobile nodes:
3 moving groups of 5 people each
2 Vehicles traveling on access roads
Tested with and without 2 aircraft
Applications
  Chat
  Video
  File Exchange
Objective Alpha
Objective Charlie
Objective Bravo
Command
Indicates FX node
1000 meters
Notes: 7

## Slide 8: CONCERTO-Baseline Comparison
533 MHz ARM Processor
256 MByte memory
5 Watts average power
800 MHz ARM Processor
256 MByte (20 Mbytes used)
7 Watts average power
Tactical Applications
Tactical Applications
802.11b PHY
802.11b PHY
CONCERTO Protocols
Baseline Protocols
Network Coding
Subgraph Computation
Reliable Forwarding
OLSR
Basic Multicast Forwarding
Nack-Oriented Reliable Multicast
Compare
Common applications and PHY allow “apples-to-apples” comparison

## Slide 9: Air Scenario – Distance Utility Metric
Parking Lot
Deployment
Alpha/Bravo
Bravo/Char.
Engineering
CONCERTO close to max metric during tactical phases
Baseline barely able to support local video post-deployment
7x
CONCERTO provides 7x higher performance than baseline in Air Scenario

## Slide 10: Challenges In Subgraph Construction
Requires Link State from all network
Inaccurate LS info results in inefficient or defective subgraph
Solution: subgraph construction based on local info
Gradient-based Routing
Constructs field and currents for information flow
Made possible by network coding fluid flow
Provides natural properties of (Electric) Potential Fields
  Efficient flow allocation
  Locality of perturbation, Stability
  No local minima: data never stalls in the middle

## Slide 11: Gradient-based Routing Information Flow Modeled on Electric Network
Network Level
Flow Level
Objective: Minimize total transmissions: G=Σ{all links ab} |Iab|/Qab
Iab = Information rate from a to b; Qab = P[success Tx from a to b]
Solution: Data network – equivalent to electric network:
Approximation: minimize G= Σ(Iab)2/Qab  minimize E= Σ(Iab)2Rab
Information rate from a to b  intensity of current Iab
Link quality from a to b = Qab  1/Resistance = 1/Rab
Minimize Data Transmission: reduced to minimizing total electric energy
  Classic problem of solving electric circuits

## Slide 12: BRAVO: Network Coding over Gradient-based Subgraphs
Netcoded data over gradient routes gains from multipath, opportunistic network usage
Selective Tx
(no flooding)
Opportunistic Rx
Multipath
reliability
Local reliability
Multipath enables
robust mobility
Routing Challenges
Reduced overhead through local info
Multipath increases stability
Data Transport Challenges
Selective Tx is efficient
Opportunistic Rx increases Tx efficiency
Local & multi-path reliability increases end-end goodput effectiveness

## Slide 13: BRAVO Performance
The Gauntlet Scenario
20 nodes, 2 stationary, 18 moving in random in regions
Scenario | Mean duration [s] | Std dev [s]
Full speed | 42.275 | 54.530
Half speed | 80.338 | 88.238
Quarter speed | 138.518 | 143.131

## Slide 14: BRAVO Outperfroms SMF + NORM
BRAVO robust at high speeds
Why:
Gradient-based subgraph ajdusts locally to topo changes
Multi-path routing compensates the temporary lack of a link
Network Coding adds redundancy: help deliver data, no matter where they come from

## Slide 15: Conclusions
Gains achieved besides information theoretical
Network Coding enables multi-path reliability
Network Coding enables hop-by-hop reliability
Gradient-based subgraph routing
  More efficient and scalable multipath routing

## Slide 16: BACKUP

## Slide 17: Intra-Session Coding: Wireline Butterfly
Unit link capacities
S
D1
D2

## Slide 18: Wireline Butterfly with Multicast Routing
Unit link capacities
S
D1
D2
Flow of rate 2
Flow of rate 2
Multicast to D1 and D2:
Can we support two flows of rate 2 with unit link constraint?

## Slide 19: Wireline Butterfly with Intra-Session Network Coding:
Unit link capacities
S
D1
D2
<A, AB ><A,B>
<B, AB ><A,B>
A
A
B
B
B
A
AB
AB
AB
Routing: Sum of “per destination” flows on a link must be less than link capacity
Network Coding: Maximum over “per destination” flows on a link must be less than link capacity
We can support “full rate” multicast to both destinations by XORing packets

## Slide 20: Wireless Butterfly with Multicast Routing
Lossless links
S
A
B
C
D1
D2
Routing: Sum of Tx Rates / symbol = 4
Contention-free schedule: S, A, B, C
1
1
1
1

## Slide 21: Wireless Butterfly with Intra-Session Network Coding
Lossless links
S
A
B
C
D1
D2
NC: Sum of Tx Rates / symbol = 2.5
Contention-free schedule: S, S, A, B, C
(Routing: Sum of Rates = 4)
AB
B
A
½
½
½
1
(A,B)

## Slide 22: Wireless Butterfly with Intra-Session Network Coding
Lossy links
S
A
B
C
D1
D2
Ploss=50%
Rate = (1-0.52)-1 = 4/3
When links are lossy, need only send at rate which transfers info to some next node on the other side of a cut set…

## Slide 23: Intra-Session Network Coding
Ahlswede et al. proved that for a single multicast session, network coding achieves the maximum possible rate allowed in the network
Problem Decomposition
  Computing Mixtures
    How to combine packets into mixtures that “work”
  Subgraph Construction
    Which nodes forward mixtures and how much do they participate

## Slide 24: Computing Mixtures: Random Linear Coding
Ho et al.: Random Linear Coding
  Encoding:
  Identity of packets received – does not matter
  Only matters: Quantity of mixed packets = group size
Practical Network Coding (Chou et al.)
  Break file into N packets
  Collect packets into groups of G packets (generations)
  Source/intermediate nodes transmit random mixtures from generations
  Innovative (linearly independent) packets are stored for future mixtures
  Packet headers collect coefficients used in random coding
  Destination collects G linearly independent coded packets
  Inverts the matrix of random coefficients to recover original packets
Intra-session coding is basically matrix inversion
src
R1
dst
R2
α P1+ ß P2
γ P1+ δ P2
P1
P2
P1
P2

## Slide 25: Subgraph Construction
Not all nodes in a network should participate in each multicast flow
  Want to maximize network capacity by minimizing transmissions
Subgraph
  The nodes which participate in random linear coding for a multicast flow
  The rate at which these nodes forward random linear combinations
D
S
Can contribute significantly
to info advance to D
Can not contribute
significantly
to info advance to D
Rij
Forwarding intensity:
Assigned Information rate

## Slide 26: Subgraph Computation: Optimization Problem
Optimal Subgraph computation is complex (exponential in no. neighbors)
netcoded transmissions on link (i, j) greater than maximum per dest flow
conservation of flow to destination t at node i
link capacity constraints
Convex cost function can capture goals of minimum energy, congestion, cost or maximum throughput

## Slide 27: Video Utility - Ground
Baseline
CONCERTO
LZ
Deploy
Alpha/Bravo
Bravo/Charlie
Engineering
100
100
82
94
61 42 39
90 90 88
82 60 43
95 90 94
40 33 28
92 85 54
Ave. Utility
Baseline barely usable at lowest load; CONCERTO works well at highest tactical loads

## Slide 28: Video Utility - Air
Baseline
LZ
Deploy
Alpha/Bravo
Bravo/Charlie
Engineering
100
100
82
94
66 51 46
90 90 83
83 56 53
93 89 89
39 33 29
89 78 73
Ave. Utility
Maximum Throughput Utility
CONCERTO
Baseline barely usable at lowest load; CONCERTO works well at highest tactical loads