## Slide 1: OSPF Extensions for Link State Database Synchronization Group draft-ylz-ospf-lsdb-sync-group-00
Gang Yan, Yuanjiao Liu, Xudong Zhang
Huawei Technologies
IETF 86, Orlando, FL, USA

## Slide 2: Background Introduction
Devices of access layer have the following characteristics:
  Huge devices.
  Performance is not enough to support the big LSDB and the big routing table.
Backbone Area
………
………

## Slide 3: Cost of System
Access Device
  Poor CPU and Less Memory.
  Can not support many routes.
  Can not process many flooding packets.
Aggregate Device
  500 – 1000 peers or more.
  Too many flooding process.
    Stability of neighbor
    Convergence time
Multiple Area?
  Is it ABR router? Schedule Problem?
  SPF schedule, Summary LSA generate and Route aggregate.

## Slide 4: Method: Sync Group
Goal: Reduce the usage of CPU/Memory of the access device and traffic of flooding.
Sync Group = Area in Area.
The adjacency only is made between the routers with same group ID.
The LSDB will be synchronized within Sync Group only.
The “Group Member Router” will add the default route to the nearest “Group Master Router”.
The LLS is used to indicate the router support SYNC GROUP.
The RI LSA is used to indentify the “Group Master Router”.
Backbone Area
Area 1
Sync Group 1
Sync Group 2
Group Member Router
Group Master Router

## Slide 5: OSPF extension
New TLV will be added to LLS.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type(TBD) | 4 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Synchronization Group ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
New TLV in Router Information LSA
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Synchronization Group ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Synchronization Group ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Flags (2 octet):
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved |S|M| (M - Group Master/Member Role bit)
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: Challenge: Inconsistency of LSDB
There exists inconsistency!
The path from RTA to RTB?
  RTA to RTC to RTB?
  RTA to RTD to RTF to RTE to RTB?
  How to avoid the route loop?
Method 1: Routing calculation of RTA/RTB/RTC (The router is not in SYNC group) are modified to avoid the path through the SYNC group.
Method 2: Update the router LSA of “Group Master Router” to remove the link to “Group Member Router”. And associated SPF process also need be updated.
Area x
100
10
100
10
10
10
RTA
RTB
RTC
RTD
RTE
RTF
RTG

## Slide 7: Next Steps
Keep on research to get final solution about path calculation.
Welcome comments on mailing list.