## Slide 1: OSPFv3: Homenet and Data Centers
Fred Baker

## Slide 2: Homenet Requirements
Homenet is trying to develop supporting technologies for a very simple, but technologically advanced, home
  Primarily focused on IPv6
  Zero Configuration if at all possible
  Interface to Smart Grid technologies including Zigbee/802.15.4
  Multi-subnet with routing an option
  Potentially multihomed to multiple ISPs
  Edge Routing to resolve BCP 38 issues

## Slide 3: I have been asked about OSPF-Multi-Topology
Topologies are defined by metrics on links between router interfaces within the routing domain
  The link does or does not have a metric within the topology
  Automatically routes around discrepancies between physical and logical topology
A number of source/destination routing cases could be implemented as multi-topology
Edge routing is routing to a default route that is outside the routing domain
  The OSPFv3 topologies for each PA prefix are identical
  There is no link advertised in OSPFv3 that might have the indicated metric
Edge routing is a reachability problem, not a topology problem

## Slide 4: Context
RFC 5340 defines three prefix LSAs
  Fixed format, which makes it hard to add information to them
I’m looking at
  Homenet requirements for egress routing
  Multi-tenant Data Center requirements for tenant-to-tenant access control

## Slide 5: draft-baker-ipv6-ospf-extensible
I defined three extensible LSAs, replacements for intra-area-prefix-LSA, inter-area-prefix-LSA, and AS-external-LSA
I have since been told of Abhay Roy’s extensible LSA draft in draft-ietf-ospf-mt-ospfv3 (2007)
I’ll use whatever extensible technology the WG approves

## Slide 6: Flow label and Source Address sub-TLVs
Premise:
  Reachability TLV, with sub-TLV(s), identifies a set of possible messages to send down a route
  Need comments on route calculation and FIB design

## Slide 7: Route Calculation
Normal OSPFv3 route calculation:
  Identifies a sequence of routers and links from calculating router to router advertising TLV
  “Router” might be a Network LSA
LSA, in this case, identifies not only the destination but a qualification
  Traffic with a different source address or flow label follows a different route, or no route

## Slide 8: Backward compatibility
Acee asked about making this work in networks with RFC 5340 format LSAs as well
Really not a problem:
  Definition of source prefix sub-TLV:
    A zero-length LSA (::/0) can be represented with a sub-TLV whose length is zero or no sub-TLV
  Definition of flow label sub-TLV:
    “any” flow label is specified by leaving the sub-TLV out
RFC 5340 LSA by definition leaves those sub-TLVs out. Semantically equivalent.

## Slide 9: FIB Design
Not subject to standardization.
Some suggestions in an appendix
  Linux (Waikato extensions) has separate FIBs by source prefix.
    One could insert destination into appropriate FIB, or all FIBs if source not specified
  PATRICIA tree
    Allows a discontiguous bit string, differing don’t-care sets
    Recursive descent following most useful bits
    Final answer compared to entire specification

## Slide 10: Possible use cases
Source Prefix
Egress Routing
  Most TLVs in network destination-only
  Default routes to upstream specify PA source prefix
One could imagine more general uses, such as dynamic “ACL”
Flow Label (RBAC model)
Long discussion about use of the Flow Label in the IETF, with many suggestions
One could also use it as a tenant id in a multi-tenant data center
  IPsec or TLS still required for proper end-to-end security
  Tagged route limits attack possibilities to neighbors that know the “password”