## Slide 1: PCEP Extensions for remote-initiated GMPLS LSP Setup draft-ali-pce-remote-initiated-gmpls-lsp-00.txt
Author list:
  Zafar Ali (zali@cisco.com) - Presenter
  Siva Sivabalan (msiva@cisco.com)
  Clarence Filsfils (cfilsfil@cisco.com)
  Robert Varga (Pantheon Technologies)
  Victor Lopez (vlopez@tid.es)
  Oscar Gonzalez de Dios (ogondio@tid.es)
86th IETF, PCE WG, Orlando, FL, USA (March 2013)

## Slide 2: Outline
Scope
Use cases
Requirements
Solution
Next Steps

## Slide 3: Scope
PCEP Extensions for PCE-initiated GMPLS LSP Setup in a Stateful PCE Model.
Extends draft-crabbe-pce-pce-initiated-lsp for GMPLS LSPs and multilayer networks.
When an active stateful PCE is used for managing remote-initiated LSP, the PCC may not be aware of the intended usage of the remote-initiated LSP.
  This draft also addresses the requirement to specify on how PCC should use the PCEP initiated MPLS or GMPLS LSPs.

## Slide 4: Outline
Scope
Use cases
Requirements
Solution
Next Steps

## Slide 5: Single-layer provisioning from active stateful PCE
The active PCE can dynamically create or delete L0 services between client interfaces.
New connections or reoptimization is controlled by stateful PCE(s).

## Slide 6: Bandwidth-on-demand for multi-layer networks
A multilayer stateful PCE(s) establishes L0 circuits based on L3 demands.
PCE computes the L0 Paths and triggers L0 circuit creation.
Bandwidth on demand and spare bandwidth is shared.

## Slide 7: Higher Layer Signaling Trigger
Similar to the previous use case but in this scenario a L3 PCE is used.
PCE triggers L0 circuit creation but GMPLS signaling takes care of path computation and establishment of the LSP.

## Slide 8: NMS-VNTM cooperation model
NMS does not have information about all network information, so it consults L3 PCE.
In case of there is no path in L3; NMS sends a message to the VNTM to create a GMPLS LSP at the lower layer.

## Slide 9: Outline
Scope
Use cases
Requirements
Solution
Next Steps

## Slide 10: GMPLS Requirements for Remote-Initiated LSPs
Support for multiple switching capabilities.
Support for encoding type to be used by the LSP.
Support for G-PID to be carried by the LSP.
Technology specific Traffic Parameters.
Support for Asymmetric Bandwidth.
Support for unnumbered interfaces [RFC3477].
Explicit label control.
GMPLS protection and restoration [RFC4872], [RFC4873], etc.

## Slide 11: Remote Initiated LSP Usage Requirement
The target IGP instance for the Remote-initiated LSP.
In the target IGP instance, should the PCE-initiated LSP be advertised as a forwarding adjacency and/ or routing adjacency and/ or to be used locally by the PCC?
If Remote-initiated LSP is to be advertised an IPv4 FA/ RA, IPv6 FA/ RA, what is the local and remote IP address is to be used for the advertisement

## Slide 12: Outline
Scope
Use cases
Requirements
Solution
Next Steps

## Slide 13: PCEP Extensions for Remote-Initiated GMPLS LSPs
LSP create message defined in [I-D. draft-crabbe-pce-pce-initiated-lsp] is extended to include GMPLS specific PCEP objects.
Minor misc. changes to support GMPLS initiated LSPs.

## Slide 14: PCEP extension for PCE Initiated LSP Usage Specification
[RFC6107] defines LSP_TUNNEL_INTERFACE_ID Object for communicating usage of the forwarding or routing adjacency from the ingress node to the egress node.
This document extends the LSP Create Message to include LSP_TUNNEL_INTERFACE_ID object defined in [RFC6107].

## Slide 15: Communicating LSP usage to Egress node
PCE does not need to send LSP Create message to egress node to communicate LSP usage information.
Instead PCC uses RSVP-TE signaling mechanism specified in [RFC6107] to send the LSP usage to Egress node.

## Slide 16: Outline
Requirements and Scope
Problem Statement
Solution
Next Steps

## Slide 17: Next Steps
We would like to request PCE WG Charter to include this work.

## Slide 18
Thank You.