## Slide 1: Extension of the MLD proxy functionality to support multiple upstream interfaces <draft-contreras-multimob-multiple-upstreams-01.txt>
1
Luis M. Contreras
Telefónica I+D
Carlos J. Bernardos
Universidad Carlos III de Madrid (UC3M)
Juan Carlos Zúñiga
InterDigital
Orlando, PIM WG, March 2013

## Slide 2: Problem statement
86th IETF, Orlando
General application:
  Sharing of a common network access infrastructure among different multicast content providers
Advantages
  Subscribers can get their preferred contents from different multicast content providers without network constraints and without requiring PIM routing on the access / aggregation device
  Redundancy
2
Multicast Content Provider A
Multicast Content Provider B
MLD proxy

## Slide 3: Motivation
86th IETF, Orlando
The support of multiple upstream interfaces on an MLD proxy functionality has been identified as an opportunity for system optimization
Complexity
  Handling of control messages for/from multiple upstreams
  Efficient handling of data traffic for/from multiple upstreams
Purpose
  Identification of requirements for supporting multiple upstreams
  Specification of the needed MLD proxy functional extensions
Changes from last version
  Fixed network communication scenarios introduced
  PMIPv6 appendix included for explanatory introduction to mobile scenarios (MULTIMOB-centered)
3

## Slide 4: Fixed network communication scenarios
  Fixed broadband based
  Multicast wholesale offer for residential services
    Complementary multicast service offered by alternative operators in an efficient manner
  Multicast resiliency
    Path diversity through the connection to distinct leaves in a given multicast tree (skipping routing based mechanisms)
  Load balancing for multicast traffic in the metro network
    Demand split on different paths
  Benefits
    Resource efficiency on distribution network
    Avoidance of multicast routing complexity as far as possible from the access / aggregation devices
4
86th IETF, Orlando

## Slide 5
Needed functionality per fixed scenario
85th IETF, Atlanta
 | Fixed Network Scenarios |  | 
Functionality | Multicast Wholesale | Multicast Resiliency | Load Balancing
Upstream Control Delivery |  |  | 
Downstream Control Delivery |  |  | 
Active / Standby Upstream interface |  |  | 
Upstream i/f selection per mcast group |  |  | 
Upstream i/f selection for all groups |  |  | 

## Slide 6: Mobile network communication scenarios
  First, a short introduction on Multicast listeners with Proxy Mobile IPv6 (MULTIMOB WG’s scope) …
6
86th IETF, Orlando

## Slide 7: Proxy Mobile IPv6 (RFC 5213)
MN 1’s attachment
detected by MAG 1
LMA looks for MN 1 ID in its table
MN 1 ID | MN 1’s assigned prefix | MAG 1’s IP address
LMA adds an entry for MN 1 ID in its table
(IPv6 forwarding is also set-up for the assigned prefix)
Proxy BA
Router Advertisement (prefix)
MN 1 configures an
IPv6 address based
on received prefix
Router Solicitation
Proxy BU
7
86th IETF, Orlando

## Slide 8: Proxy Mobile IPv6 (RFC 5213)
MN 1’s dettachment
detected by MAG 1
LMA looks for MN 1 ID in its table
MN 1 ID | MN 1’s assigned prefix | MAG 1’s IP address
LMA sets a timer to delete entry for MN 1 ID
from its table
Router Advertisement (prefix)
LMA looks for MN 1 ID in its table
LMA updates the entry for MN 1 ID in its table
(IPv6 forwarding is updated for the assigned prefix)
MN 1 ID | MN 1’s assigned prefix | MAG 2’s IP address
MN 1 keeps using the
same IPv6 address
MN 1’s attachment
detected by MAG 2
MN 1 keeps using the
same default router
8
86th IETF, Orlando
Proxy BA
Proxy BA
Router Solicitation
Proxy BU
Proxy BU

## Slide 9: A Minimal Deployment Option for Multicast Listeners in PMIPv6 Domains (RFC 6224)
9
86th IETF, Orlando
One MLD proxy instance per LMA
Remote subscription at the LMAs
The MN is associated with one LMA

## Slide 10: Mobile network communication scenarios
  PMIPv6-based (MULTIMOB)
  Listener mobility
    Single MLD proxy instance on MAG per LMA
    Remote and local multicast subscription
    Dual subscription to multicast groups during handover
  Source mobility
    Support of remote and direct subscription in basic source mobility
    Direct communication between source and listener associated with distinct LMAs but on the same MAG
    Route optimization support in source mobility for remote subscribers
  Benefits
    Traffic routing optimization within the PMIPv6 domain
    Simultaneous support of remote and local multicast subscription
    Avoidance of multiple MLD proxy instances on MAG
10
86th IETF, Orlando

## Slide 11
Needed functionality per mobile scenario
85th IETF, Atlanta
 | Multicast Listener |  |  | Multicast Source |  | 
Functionality | Single MLD proxy | Remote & Local Subscr. | Dual Subscr. during HO | Direct & Remote Subs. | Listener & Source on MAG | Route Optimiz.
Upstream Control Delivery |  |  |  |  |  | 
Downstream Control Delivery |  |  |  |  |  | 
Upstream Data Delivery |  |  |  |  |  | 
Downstream Data Delivery |  |  |  |  |  | 
1:1 MN to Upstream Association |  |  |  |  |  | 
1:N MN to Upstream Association |  |  |  |  |  | 
Upstream i/f selection per mcast group |  |  |  |  |  | 
Upstream i/f selection for all groups |  |  |  |  |  | 
Upstream traffic replication |  |  |  |  |  | 

## Slide 12: Proposed next steps
86th IETF, Orlando
Collect pending / potential scenarios not yet covered for both fixed and mobile network communications
Receive comments on documented requirements, and identify new ones, if not yet raised
Start describing MLD proxy extension to cope with required functionality
Move the draft proposal to PIM WG
  Prepare -00 version for PIM WG after Orlando meeting addressing received comments and feedback
12