## Slide 1: PIM VRRP Interoperability
draft-zhou-pim-vrrp-01
Wei Zhou
IETF 86, Orlando

## Slide 2: Rationale
PIM has no inherent redundancy capability.
PIM operation is completely independent of First Hop Redundancy Protocols (FHRP) such as VRRP and HSRP.
There is a need to enable IP multicast forwarding resiliency in redundant network with VRRP enabled.
  Make Master router the DR after VRRP failover such that Master router is the one responsible for maintaining mroute states and multicast forwarding.
  Make VRRP Master router the one responsible for processing PIM J/P messages targeting VRRP virtual IP address.

## Slide 3: Use Case
A
B
C
H1
H2
A and B are routers running VRRP
C is the virtual router address
A and B need to adjust PIM DR priority depending on who is Master
Need interaction between PIM and VRRP
X
Downstream router X has a static route with C as next-hop.

## Slide 4: Proposed Solution
Allow PIM to track VRRP group on an interface
  Leverage VRRP’s capability to track uplink status
PIM DR priority adjustment
  Adjust DR priority to a configured value when becomes VRRP Master, allows DR be predictable before and after a switchover
  Make VRRP Master the DR, process IGMP Join and start forwarding traffic

## Slide 5: Tracking & Failover
PIM keeps tracking VRRP state
  Upon VRRP switchover, new Master router sends PIM Hello with new GenID using Virtual IP as source address
  Trigger downstream routers to send PIM Join to virtual IP
  Only Master router will process PIM Join, create mroute state and pull traffic from upstream and start forwarding
  Backup routers ignore PIM Join/Prune messages targeting the Virtual IP

## Slide 6: Tracking and Failover Proposed change in rev-01
PIM keeps tracking VRRP state
  All passive routers:
    Maintain mroute states
    Record the GenID of current Master router
  Upon VRRP switchover, new Master router uses the existing mroute states and recorded GenID from previous Master router in its PIM Hello message.
  No action required on downstream routers.

## Slide 7: Tracking and Failover Proposed change in rev-01
Advantages comparing to original solution:
  This solution make switchover completely transparent to downstream routers.
  Avoids resending PIM J/P upon switchover from downstream routers.
  No need to re-create mroute states on new Master router.
  Potentially faster convergence upon switchover.

## Slide 8: PIM Assert
If only one VRRP group, Backup routers will send a large penalty metric preference (PIM_ASSERT_INFINITY - 1) and make MR the Assert winner.
If there are multiples VRRP groups configured on an interface, Assert metric preference will be (PIM_ASSERT_INFINITY - 1) if and only if all VRRP groups are in Backup.
If there is at least one VRRP group in Master state on an interface, then original Assert metric preference will be used.

## Slide 9: BiDir Group
If only one VRRP group, Backup routers will send a large penalty metric preference in Offer (PIM_BIDIR_INFINITY_PREF- 1) and make MR the DF winner.
If there are multiples VRRP groups configured on an interface, Offer metric preference will be (PIM_BIDIR_INFINITY_PREF- 1) if and only if all VRRP groups are in Backup.
If there is at least one VRRP group in Master state on an interface, then original Offer metric preference to RP will be used.

## Slide 10: Further Considerations
Support of HSRP
  The proposed scheme can also enable HSRP aware PIM with similar switchover and tracking mechanism described here