## Slide 1: PIM Join Attributes for LISP
draft-arango-pim-join-attributes-for-lisp-00
Jesus Arango Stig Venaas Isidor Kouvelas
IETF 86, Orlando, Florida

## Slide 2: Problem Being Solved
LISP multicast (RFC6831) defaults to multicast transport over the RLOC core
However, implementations are initially focusing on unicast transport with head-end replication at the root site
Support LISP multicast over core networks that do have native multicast support
Support mixed environments where some receivers have core multicast connectivity and some do not

## Slide 3: RFC-6831 PIM Signaling
S
ITR
D
ITR
ETR
ETR
RLOC core
S1
S2
D1
D2
12.0.0.2
13.0.0.2
10.0.0.1
11.0.0.1
R11
R1
R2
R12
ETR
R21
ETR
R22
ETR
ETR
R3
11.0.0.11
13.0.0.12
13.0.0.21
13.0.0.22
(S-EID,G)
PIM JP
(S-EID,G)
PIM JP
(S-EID,G)
PIM JP
(S2-RLOC,G)
PIM JP
(S-EID,G)
PIM JP
1.0.0.1
(S2-RLOC,G)
PIM JP
Legend:
EIDs -> Green
Locators -> Red
site or core
PIM router
regular PIM JP
unicast PIM JP
(S-EID,G)
PIM JP

## Slide 4: Unicast Transport
Unicast Transport with head-end replication at the root-ITR only uses Unicast LISP encapsulated (S-EID,G) J/P from receiver-ETR to root-ITR (no native PIM J/P over RLOC core)
Unicast transport requires the communication of two additional pieces of information in the PIM (S-EID,G) Join message:
  An indication that the receiver-ETR wants unicast transport and is not additionally joining through native multicast by sending an (S-RLOC,G) Join
  The receiver-ETR RLOC address that should be used as the destination for the LISP unicast encapsulated multicast data packets

## Slide 5: Encoding Receiver-ETR RLOC
No options in current LISP encapsulated PIM J/P message format
Outer and inner IP header source addresses cannot be used to carry receiver-ETR RLOC
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| IHL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol = 17 | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Routing Locator |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Routing Locator |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Port = xxxx | Dest Port = 4341 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| UDP Length | UDP Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|N|L|E|V|I|flags| Nonce/Map-Version |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instance ID/Locator-Status-Bits |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| IHL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source EID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination EID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|PIM Ver| Type | Reserved | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Upstream Neighbor Address (Encoded-Unicast format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Num groups | Holdtime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Multicast Group Address 1 (Encoded-Group format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Number of Joined Sources | Number of Pruned Sources |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Joined Source Address 1 (Encoded-Source format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ... |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
OH
UDP
LISP
IH
PIM

## Slide 6: Outer IP Source Unsuitable
Outer (LISP encapsulation) IP header source address is determined by routing
The receiver-ETR interface that the join message is sent out of is determined by the routing information for the root-ITR RLOC
The outer header IP source address:
  Must be the address of the interface that the encapsulated message is being transmitted on to avoid URPF issues
  Must be of the same AF as the selected root-ITR RLOC

## Slide 7: Inner IP Source Unsuitable
Inner (PIM message) IP header source address must be of EID address family and cannot be used to carry an RLOC AF address
RFC-4601 mandates that PIM J/P message IP header is of the same AF as the encoded group and source addresses that it carries
The header must be of EID AF to ensure correct processing when received within the EID VRF of the root-ITR post LISP decapsulation

## Slide 8: PIM J/P Attribute Solution
  PIM Join/Prune attributes can be used to carry additional information in a PIM J/P message (RFC 5384 + draft-venaas-pim-hierarchicaljoinattr)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|PIM Ver| Type | Reserved | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Upstream Neighbor Address (Encoded-Unicast format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Num groups | Holdtime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Multicast Group Address 1 (Encoded-Group format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Number of Joined Sources | Number of Pruned Sources |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Joined Source Address 1 (Encoded-Source format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ... |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Attributes can be encoded on:
  The Upstream Neighbor Address
  A Multicast Group Address
  A Joined or Pruned Source Address

## Slide 9: Encoding LISP Unicast Transport Information as PIM J/P Attributes
We are defining two new PIM Join / Prune attributes:
  The Transport Attribute conveys the receiver-ETR choice of unicast transport over multicast
  The Receiver RLOC Attribute conveys the receiver-ETR RLOC that should be used as the target for the LISP encapsulated multicast data

## Slide 10: Transport Attribute Format
Transport field is set to 0 for multicast transport and is set to 1 for unicast transport.
0 1 2
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|F|E| Type = 5 | Length = 1 | Transport |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 11: Receiver RLOC Attribute Format
Address Family field carries the PIM Address Family of the receiver RLOC as defined in RFC4601
Receiver RLOC field carries the RLOC address on which the receiver xTR wishes to receiver the unicast-encapsulated flow
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|F|E| Type = 6 | Length | Addr Family | Receiver RLOC
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-...

## Slide 12: Wrap Up
Adding support for unicast transport to LISP multicast PIM signaling
Introducing the Transport and Receiver RLOC attributes to carry additional required information in LISP encapsulated (S-EID,G) Join/Prune PIM messages