## Slide 1: PW Endpoint Fast Failure Protection draft-shen-pwe3-endpoint-fast-protection-03
Yimin Shen (Juniper)
Rahul Aggarwal (Arktan Inc)
Wim Henderickx (Alcatel-Lucent)
IETF 86, Orlando

## Slide 2: Update
The new revision provides high-level guidelines for IGP advertisement and path computation for context IDs.
  Allows a range of options.
  Considers specific option as out of scope.
  Provides flexibility to accommodate existing and future approaches, which may be generic to egress protection for all layer-2/3 VPNs.

## Slide 3: Motivation
It is important to have local repair (aka. fast reroute) mechanisms protect every link and node along a PW.
This draft provides a such kind of mechanism for protecting egress AC, egress/terminating PE, and switching PE.
  The final piece for a complete solution for end-to-end service restoration in 10s of milliseconds.
  Complements global repair.
CE1
CE2
PE1
PE2
PW
S-PE1
seg-1
seg-2
PW traffic
AC
AC

## Slide 4: Highlights
Single- and multi-segment PWs.
RSVP, LDP and IP transport tunnels and bypass tunnels.
Upstream label assignment and context label switching.
LDP Extension
  Protection FEC Element TLV, for FEC 128 and 129.
Efficiency and scalability
  Co-located protector model
  Centralized protector model

## Slide 5: How it works
PE distributes PW label to a protector via LDP extension.
Protector installs PW label in a context label table.
Upon detecting a failure, PLR redirects PW packets to protector via a pre-established bypass tunnel, with PW label intact.
Protector looks up PW label in context label table, and sends packets to target CE.
Context ID
  Identifies a pair of <primary PE, protector>.
  Serves as a forwarding context, indicating the primary PE’s label space to the protector.
  Serves as destination for transport tunnel and bypass tunnel, to facilitate path computation.

## Slide 6: Scenario 1: Egress AC failure
PLR is the primary PE (PE2). It has established a bypass to protector (PE4).
Protector (PE4)
  Learns PW1’s label X from PE2 via the LDP extension.
  Installs a FIB entry for label X in a context label table. Nexthop is CE2.
  Assigns a UHP label Y for the bypass, pointing to this context label table.
Local repair:
  PE2 redirects PW packets through the bypass.
  PE4 receives packets with outer label Y and inner label X.
  PE4 looks up label X in the context label table, and sends packets to CE2.
CE1
CE2
PE1
PE2
PLR
PW1 (label=X)
PW2 (backup)
PE4
protector
PE3
bypass
label=Y
In-label | Next-hop
X | pop, CE2

## Slide 7: Scenario 2: Egress (T-)PE failure
PLR is the penultimate hop router. It has established a bypass to protector (PE4).
Protector (PE4)
  Learns PW1’s label X from PE2 via the LDP extension.
  Installs a FIB entry for label X in a context label space. Nexthop is CE2.
  Assigns a UHP label Y for the bypass, pointing to this context label table.
Local repair:
  PLR redirects PW packets through the bypass.
  PE4 receives packets with outer label Y and inner label X.
  PE4 looks up label X in the context label table, and sends packets to CE2.
CE1
CE2
PE1
PE2
PE3
PE4
protector
PW1 (label=X)
PW2 (backup)
PLR
bypass
label=Y
In-label | Next-hop
X | pop, CE2

## Slide 8: Scenario 3: S-PE failure
PLR is the penultimate hop router of seg-1. It has a bypass to protector (S-PE2).
Protector (S-PE2)
  Learns PW1’s label X from S-PE1 via the LDP extension.
  Installs a FIB entry for label X in a context label table. Nexthop is seg-4.
  Assigns a UHP label Y for the bypass, pointing to this context label table.
Local repair:
  PLR redirects PW packets through the bypass.
  S-PE2 receives packets with outer label Y and inner label X.
  S-PE2 looks up label X in context label table, swaps to label Z, pushes a transport label to PE4.
CE1
CE2
PE1
PE2
PE3
PE4
PLR
bypass
label=Y
S-PE1
S-PE2
protector
seg-3
seg-4, label=Z
seg-2
seg-1, label=X
In-label | Next-hop
X | swap Z, push T-label to PE4

## Slide 9: Next steps
Continue to solicit comments.
The document has been stable.
Would like to ask for WG adoption.