## Slide 1: Coupled congestion control for RTP media
draft-welzl-rmcat-coupled-cc-00 (01)
RMCAT, 86th IETF Meeting
11. 11. 2012
Michael Welzl
michawe@ifi.uio.no

## Slide 2: Context
Addresses “identifying and controlling groups of flows”
  “Identifying” trivial for some rtcweb flows, else requires Shared Bottleneck Detection (SBD) – working on it, hopefully first draft @ IETF87
Has been tried in the past (CM (RFC 3124), RFC 2140 ) – what has gone wrong?
  Not able to address the “identifying” part
  Too hard to implement (note: easy-to-implement, non-critical parts of RFC 2140 are actually implemented AFAIK, e.g. sshthresh caching (+ sharing?))
Try to make it as easy to implement + simple as possible

## Slide 3: “Flow State Exchange” (FSE)
The result of searching for minimum-necessary-standardization: passive storage, only define what goes in / out + what to do with the information
  So far, sender-side only
  Could reside in a single app (e.g. browser) and/or in the OS
CM
Stream 1
Stream 2
Stream 1
Stream 2
FSE
Traditional CM
FSE based flow coordination
For some rtcweb flows (trivial SBD)
SBD
Stream 1
Stream 2
FSE
FSE based flow coordination

## Slide 4: “Flow State Exchange” (FSE) /2
Flows update it when they start and stop
Flows query+update whenever they update their rate
  flow’s used rate = UPDATE(CC-calculated rate (CR), desired rate (DR))
# | FG | P | CR | DR | S_CR | Rate
1 | 1 | 1 | 8 | 2 | 10 | 2
2 | 1 | 0.5 | 3 | 3 | 11 | 9
Stored
Example state:

## Slide 5: Algorithm in the draft
Just an example – could be changed, as long as the same is used for all flows
  Perhaps best to implement with the FSE, not with each flow
Goals of the example algorithm:
  Realize fairness with priorities
  Good capacity usage: always use all the available bandwidth that congestion controls have found
  Reduce delay: N flows should not probe N times
  Let greedy flows immediately use unused bandwidth of non-greedy or terminated ones

## Slide 6: Example using older variant of the alg.: 2 vic instances w / TFRC + FSE
Without
With

## Slide 7: Current state of things
Playing with the current algorithm
  Working on 2 main FSE problems:
  A flow is told to use a rate that is not what the congestion controller has determined
    Smaller: can cc. cope with non-greedy sources? (note: on-the-wire effect probably close to greedy)
    Larger: really unusual
    Need to check congestion controls one by one
  Problems could arise when flows are highly asynchronous (async. RTTs, ..)
    Negative impact can certainly be bounded

## Slide 8: Really only on the sender side?
Reducing feedback frequency would require a message to the receiver based on information from the FSE (similar to async. RTT)
Shared Bottleneck Detection needs signaling of measurement results
  A tricky problem by itself… but not fully solving it yields false negatives, which are not too problematic (limits FSE benefits)
H1
H3
H2

## Slide 9: Thank you! Questions?