## Slide 1: LFA Manageability draft-litkowski-rtgwg-lfa-manageability-01
Stephane Litkowski Orange
Bruno Decraene Orange
Clarence Filsfils Cisco Systems
Kamran Raza Cisco Systems

## Slide 2: Content of the document (reminder)
Policy based LFA selection (§3.2) :
  Tie-breakers for selecting the LFA are not flexible enough to accommodate for all cases.
  Calling for a policy based LFA selection, controlled by the SP according to local constraints
  Based on multiple criterions with a default but customized relative order of preference.
  Applied per protected interface or set of destinations.
Operational aspects :
  Providing coverage informations
  Manual shutdown of a link
  ISIS Overload bit management (NEW)

## Slide 3: What’s new in V1 ?
Added issue with ISIS OL bit management :
We consider traffic from PE3 to PE2
PE1 does NOT satisfy Equation 1 : 100 <! 45 + 45
BUT PE1 should be considered as LFA because it cannot use PE3 as transit thanks to overload bit
Overload bit status of computing node SHOULD be taken into account while performing LFA computation
OL permanently set on PE3 to enforce routing policy

## Slide 4: What has been changed in V1 ?
We took into account all the comments, mainly :
Reduced set of new criterions, focus on :
  Link coloring
  Bandwidth
  Neighbor preference
  Remote and direct neighbors evaluated at the same level
Removed LFA SPF computation throttling

## Slide 5: Next steps
One existing implementation, two others are in the pipe
Next points to be discussed
  Signalling of information : mainly link colors, bandwidth
    Benefit of signalling ?
    Reuse existing TE extensions or define new ones ?
  Simulation tool needs to know the LFA selection algorithm :
    For LFA coverage and capacity planning
    Default implementation policy/algorithm need to be documented
    Thanks to Martin Horneffer (DT)
Sollicit WG adoption

## Slide 6: thank you