## Slide 1: Microloop prevention by introducing a local convergence delay draft-litkowski-rtgwg-uloop-delay-00
S. Litkowski, Orange
B. Decraene, Orange
P. Francois, IMDEA Networks

## Slide 2: Why this draft?
Problem
  Microloops during convergence of IS-IS and OSPF
  Actually happens, impacts traffic, notably traffic not affected by the failure itself
  Reduces IP-FRR benefits
Local-Delay
  Simple
  Incrementally deployable
  Applicable
  Partial coverage

## Slide 3: Solution: Link Down case
Rerouting node (local) lets its direct neighbors reroute away from it before FIB update
  Flood updated LSP
  WAIT
  Update FIB considering the LSP
Applicability
  Managed events
  Sudden failure of protected links

## Slide 4: Solution: Link UP Case
Reroute before telling the rest of the network
  Flood LSP/LSA with Max_Metric
  Update FIB (considering actually configured metric)
  Flood LSP with configured metric
Why step 1?
  Two-way CC

## Slide 5: Partial Coverage…
A remote microloop will not be solved
A two-hop microloop will not be solved BUT
Networks still benefit a lot from the solution
  See applicability analysis
SIMPLE!

## Slide 6: Questions?