## Slide 1: Eacp requirements
draft-retana-rtgwg-eacp
Alvaro Retana
Manuel Paul
Russ White

## Slide 2: What this Draft is not doing
Detailed use cases
Requirements specific to protocol extensions
Algorithms for optimizing energy cost of specific paths (vs. the energy footprint of the whole network)

## Slide 3: Scope and Goal of this Draft
Provide a Framework for Energy Aware Control Planes
  Considering energy awareness with regards to Control Plane design and network operation, focusing on the network requirements footprint
Catalogue proposed solutions to reduce power
  Examine impacts and possible problems caused by various mechanisms
Give guidance to designers, from a user’s perspective
  Highlight the need for satisfying end-to-end service level requirements (performance, reliability, survivability), while aggregate power demand is being reduced
Catalogue issues proposals in this space need to address
  Go between the algorithms and the techniques
  Ex.: If you’re going to propose a system that uses microsleeps, then you need to consider…

## Slide 4: Requirements (Example)
In the network illustrated, if a modification is made to the control plane in order to remove the link between R1 and R4 in order to save energy, all the destinations shown in the diagram remain reachable. However, from the perspective of R1, the best path available to reach R2 has increased in length by two hops. The original path is R1->R2, the new path is R1->R3->R4->R2. This represents a stretch of 2.
….
Designers who propose modifications to control plane protocols to achieve network energy efficiency SHOULD analyze the impact of their mechanisms on the stretch in typical network topologies, and SHOULD include such analysis when explaining the applicability of their proposals.
/---R2---\ /---\
R1 R4 R5
\---R3---/ \---/

## Slide 5: Status & Next Steps
Changes between the -00 and -01 versions.
  Updated authors' contact information.
  Modified some of the rfc2119 keywords.
Review and add to fill in where needed
  Impact of virtualization vs. equipment footprint