## Slide 1: Session Recording (SIPREC) Protocol (draft-ietf-siprec-protocol-09)
Leon Portman leon.portman@nice.com, Henry Lum henry.lum@genesyslab.com
Charles Eckel <eckelcu@cisco.com>, Alan Johnston alan.b.johnston@gmail.com
Andy Hutton andrew.hutton@siemens-enterprise.com
IETF 86 SIPREC WG Meeting
March 13, 2013

## Slide 2: Media Delivery from SRC to SRS
Multiple ways for SRC to deliver recorded media to SRS
  1) one RTP session for each participant in CS
    e.g. one for audio from Alice, another for audio from Bob, etc.
  2) one RTP session for each media type
    e.g. one for audio, another for video, etc.
  3) one RTP session for all media
    e.g. multiple media types from multiple participants
SRC
SRS
Options 1 and 2 MUST be supported
Option 3 out of scope as still being defined

## Slide 3: RTP Session Usages
For CS with Alice and Bob, SRC could use:
1) multiple m-lines
    one m-line for audio from Alice, another for audio from Bob
  2) mixing
    SRC combines audio from Alice and Bob into a single RTP session and sends them towards SRS using its own SSRC
  3) SSRC multiplexing
    SRC multiplexes audio from Alice and Bob into a single RTP session with multiple SSRC values
Options 1 and 2 MUST be supported
SSRC multiplexing removed from draft (was section 8.3.2)
SRC
SRS
Alice
Bob

## Slide 4: Added RTP Session Usage by SRS (section 8.4)
SRS that supports recording an audio CS MUST support SRC usage of separate audio m-lines in SDP, one per CS media direction
SRS that supports recording a video CS MUST support SRC usage of separate video m-lines in SDP, one per CS media direction
Examples:
  SRS supporting audio call MUST support receiving at least two audio m-lines
  SRS supporting audio and video call, MUST support receiving at least four total m-lines in the SDP, two audio m-lines and two video m-lines
These requirements allow implementation of SRS that supports:
  video only
  recording only one direction of one stream in a CS
    E.g. record security cameras that only send (not receive) video without any audio

## Slide 5: Authentication and Authorization
Support for TLS mutual authentication required
  Deployment decision whether to use it or not
If signaling between SRC and SRS is not direct (e.g. SIP proxy exists between SRC and SRS)
  each hop is subject to the TLS mutual authentication constraint
  transitive trust at each hop is utilized
SRC or SRS may use additional existing SIP mechanisms available, including but not limited to:
  Digest Authentication [RFC3261]
  Asserted Identity [RFC3325]
  Connected Identity [RFC4916]

## Slide 6: Media Protection
SRC and SRS MUST support the SDES key negotiation mechanism [RFC4568]
  For cases in which DTLS-SRTP is used to encrypt a CS media stream, an SRC may use SRTP Encrypted Key Transport (EKT) [I-D.ietf-avt-srtp-ekt] in order to use SRTP-SDES in the RS without needing to re-encrypt the media
SRC MAY use same or different keys in RS than in CS
  SRC may replicate RTP packets from CS to the SRS, using the same key
    SRC MUST secure SDP containing keying material in RS with at least same level of security as in CS
  SRCs that decrypt CS media stream and re-encrypt when sending to SRS
    SHOULD use different key for RS media stream than that used for CS media stream to ensure it is not possible for someone who has key for CS media stream to access recorded data they are not authorized to access