## Slide 1: Vendor Channel Protocol draft-eastlake-trill-vendor-channel-00.txt
Donald E. Eastlake 3rd d3e3e3@gmail.com
Yizhou Li liyizhou@huawei.com
Weiguo Hao haoweiguo@huawei.com
Huawei Technologies
Ayan Banerjee ayabaner@gmail.com
Insieme Networks

## Slide 2: TRILL RBridge Channel
RBridge Channel is a facility for sending typed messages between
  RBridges in the same campus
  End stations and RBridges on the same link
In the RFC Editor’s queue
  draft-ietf-trill-rbridge-channel-08.txt
Used, for example, as the envelope for BFD
  draft-ietf-trill-rbridge-bfd-07.txt

## Slide 3: TRILL RBridge Channel
Between RBridges in the same campus
Between end stations and RBridges on the same link
Link Header
RBridge Channel Header
Channel Protocol Specific Data
Link Trailer
TRILL Header
Channel Protocol #
Ethertype
Flags /Error
Ethernet Header
RBridge Channel Header
Channel Protocol Specific Data
FCS
Channel Protocol #
Ethertype
Flags /Error

## Slide 4: Vendor Channel Purpose
Will provide a way for RBridge manufactures to send messages between instances of their equipment in a TRILL campus.
This could be easier if RBridges were required to have IP addresses or MAC addresses but they are not. They have nickname(s).
RBridge Channel messages address RBridges by
  nickname, or
  data label scoped set of RBridges

## Slide 5: Vendor Channel Protocol
The Vendor Channel value in the RBridge Channel Protocol number means the Channel protocol specific data starts with a Vendor Channel Header:
  OUI to identify the vendor
  Error reporting field
  Optionally 8 bits of Vendor sub-protocol and 8 bits of version for that sub-protocol
RBridge Channel Header
Vendor Specific Data
Vendor Ch. [4?]
Ethertype
Flags /Error
Vendor Channel Header
VERR
OUI
Sub Protocol
Sub Version
RBridge Channel Protocol Specific Data

## Slide 6: END