## Slide 1: RSVP App-ID Profiles at IETF86
draft-ietf-tsvwg-rsvp-app-id-vv-profiles-00
14 March 2013
James Polk
Subha Dhesikan

## Slide 2: Scope of ID
Purpose – differentiate what traffic type is carried in each reservation
Create registered profiles using RFC 2872 RSVP Application-ID Object for each real-time traffic class defined in MMUSIC draft

## Slide 3: RSVP APP-ID Object Template
The template from RFC 2872 is as follows:
0 1 2 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PE Length (n) | P-type = AUTH_APP |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Attribute Length | A-type = | Sub-type = |
| | POLICY_LOCATOR| ASCII_DN |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Application policy locator attribute data in X.500 DN format |
| (see below) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Creates a profile that includes the following pieces of information:
“P-type = , A-type = , Sub-type = , GUID= , APP= , VER= “
The Broadcast Video Surveillance Profile
AUTH_APP, POLICY_LOCATOR, ASCII_DN,
"GUID=http://www.ietf.org/internet-drafts/
draft-ietf-mmusic-traffic-class-for-sdp-03.txt,
APP=broadcast.video.surveillance, VER="

## Slide 4: New Open issues
  No known open issues
  Addressed all issues pointed out by two recent reviews

## Slide 5: Next steps
Reviews needed
Joint WGLC (in May?) with MMUSIC draft
  TSVWG’s draft normatively references the MMUSIC draft