## Slide 1: RTCP XR Blocks for Synchronization Delay and Offset Metrics Reporting
draft-ietf-xrblock-rtcp-xr-synchronization-02
Hitoshi Asaeda (asaeda@nict.go.jp )
Rachel Huang (rachel.huang@huawei.com)
Qin Wu (sunseawq@huawei.com)

## Slide 2
Updates Since Last Version
Using signed fixed-point number for synchronization offset to imply the relation between the report stream and the reference stream.
  A positive value means the reporting stream leading before the reference stream.
  A negative one means the reporting stream lagging behind.
Clarify what is the beginning of session for initial synchronization delay
  In this document, the beginning of a multimedia session is chosen as the time when the receiver joined the first RTP session.
Other editorial changes.
WGLC finished.

## Slide 3
Confusion in Synchronization Offset Metrics Report Block
Currently, “SSRC of reference” field of RTP Flow Synchronization Offset Metric Block may be ambiguous for flows in multiple RTP sessions.
  Several flows , each of them is in a different RTP session, may be assigned with the same SSRC.
Proposals:
  Limiting to one single RTP session scenario.
    May be the best approach.
  Support both Single RTP session and multiple RTP sessions.
    Need a unique identifier, such as MSID.

## Slide 4
Next Step
Fix the issues and move forward?