## Slide 1: Discussion on MN multicast activity tracking
Luis M. Contreras
Telefónica I+D
Carlos J. Bernardos
Universidad Carlos III de Madrid (UC3M)
Berlin, MULTIMOB WG, July 2013
1

## Slide 2: Rationale
87th IETF, Berlin
Generally speaking, a tracking procedure is inherently a proactive mechanism to trigger some event according to the collected information.
Tracking the MNs multicast activity helps to proactively discriminate which MNs are subscribed to some multicast content and which are not.
  Through such differentiation, the network can implement tailored signaling flows for optimizing the signaling load in the network.
  This becomes specially relevant during handover events
2

## Slide 3: Storage of tracking information
Tracking information should be kept as simple as possible
  The target is to reduce overall signaling load, then a lite mechanism has to be designed
Multicast activity (or “on-going multicast session”) is the minimal relevant information to keep
  Current multicast subscription in terms of (S,G) pairs can change during the multicast session, then triggering significant tracking update signaling without a practical usage (only relevant during the handover event)
  Multicast activity can be signaled with just 1 bit (ON/OFF)
The LMA is a common element interacting with pMAG and nMAG in a handover event
  The Binding Cache is the best fitted element to keep track of multicast activity
  Other possible solutions could consists on a direct communication between pMAG and nMAG
3
87th IETF, Berlin

## Slide 4: Signaling
In a (faster than RFC6224) multicast handover, the nMAG needs to obtain the details of the multicast subscription which the MN had at pMAG
The pMAG will always be queried about a potential MN subscription because it is not known in advanced if the MN was maintaining a multicast subscription before attaching the nMAG
This can be avoided with a simple notification of starting and finishing multicast session by the MAG where the MN is connected
  A notification message of activity status change, with its corresponding Ack message provides the required reliability
4
87th IETF, Berlin

## Slide 5: Potential signaling load savings (case study: draf-ietf-handover-optimization)
MN tracking adds complexity but allows implementing a mechanism for selectively querying the pMAG in the reactive HO case
  The pMAG is only queried for those MNs with active multicast session during the event of handover
  No query for not multicast enabled MNs nor those multicast enabled MNs which does not have an active session when the handover occurs
However, the mechanism allows to save a significant number of signaling messages in the network
  It only performs worst in static scenarios (no HOs) and in scenarios where all the MNs maintain an active multicast session (the pMAG has to be queried anyway)
Proposal: to study tracking mechanisms (and associated signaling) as a way of optimizing Multimob signaling procedures
5
Assumptions
Total number of MNs = 1000
Messages per Activity Indication = 2
Messages for querying pMAG = 2
# messages
% of mcast active MNs
# of HO
Unawareness of multicast activity: every MN is queried from retrieving potential multicast subscription information
Region where there is no gain in using the flag A mechanism
Awareness of multicast activity: only MNs with active subscriptions are queried