## Slide 1: IETF RMCAT WG: Video Quality Metrics Discussion for Evaluation Criteria
V. S. Somayazulu (v.srinivasa.somayazulu@intel.com)
Hassnaa Moustafa (hassnaa.moustafa@intel.com)

## Slide 2: Problem Statement
Video Quality Perception is critical for end-user QoE
  Topic has been discussed in WG, but no conclusion yet on including this in the requirements or the evaluation metrics for the congestion control algorithms
  Network/transport related metrics are currently present in the evaluation criteria for Rmcat congestion control algorithms, but do not fully capture the impact on video QoE.
Purpose of this presentation:
1. Provide background on video quality metrics that can help quantify impact of congestion control on the video QoE
2. Stimulate a discussion on adoption of appropriate metrics in evaluation criteria

## Slide 3: (High Level) Summary of Evaluation Scenario Discussions in RMCAT WG
Current (evolving) direction seems to be - Evaluate overall performance, i.e., Video/Audio+ Network Congestion control algorithm
Couple of ways to include video characteristics:
  Use a traffic model that captures statistics of the video source+rate control+shaping
  Possibly use uncompressed video sequences with a live encoder (+ prescribed settings) and congestion control algo.
With either approach, we should define a means of capturing impact on the overall video QoE.

## Slide 4: Objective Metrics – Big Picture View
Background
  Objective metrics developed to mimic human perception of video, e.g., “look at the received video, and judge how good it looks”
  Distortions between source and video considered a “black box” and did not affect metric design
    Good for unbiased evaluation of encoders, etc.
  Non-reference / Reduced reference a difficult problem in this generic case
Full-reference vs. non-reference VQM
  Full reference: compare the measured video with the original uncompressed video
    PSNR, MS-SSIM, PEVQ
  Non-reference: analyze the video without a comparison
    E.g. P1202, etc.
    ITU-T G.1070
Source Video
Viewed Video
Distortions
H.264 Encode
H.264 Decode
IP (UDP) Packets
Packet Loss/Jitter
Pkt Loss Concealment
Buffer Management

## Slide 5: Video Conferencing QoE – ITU-T G.1070
ITU-T G.1070
Recommendation ITU-T G.1070 proposes an algorithm that estimates videophone quality for quality
of experience (QoE)/quality of service (QoS) planners.

## Slide 6: ITU-T G.1070 Video Quality Metric
Video quality is calculated as:
  where Icoding represents basic video quality as a function of video bitrate and frame rate
  DPplV represents degree of video quality robustness due to packet loss and PplV is the packet loss rate in %
  These quantities are calculated using a set of fixed parameters dependent on codec type, video format, key frame interval, and video display size
    G.1070 provides provisional values for H.264, VGA format, 1 second key frame interval and 9.2 inch display, coded bit rates between 400 kbps – 2 Mbps, packet loss rates < 5% and frame rates from 5-25 fps.
    Parameter values for modeling any other set of conditions would need to be derived from video quality evaluation
Further enhancements to the basic model for different codecs, display formats, content dependency, etc. have been explored, e.g.:
  [Joskowicz, 2009] Joskowicz, J. et al “Enhancements to the Opinion Model for Video-Telephony Applications”, Proc. 5th Latin American Networking Conference, pp. 87-94.

## Slide 7: Considerations on use of ITU-T G.1070
Use evaluation scenario(s) to run simulation of target congestion avoidance algorithm with a given test video sequence (trace file)
  Collect trace of packet arrival times, packet losses, at sender and receiver
  Segment data into short intervals of time (e.g. 5 seconds?)
  For each segment i:
    Calculate video bitrate sent, assume fixed frame rate
    Calculate average packet loss rate at receiver
    Calculate per-segment video quality Vq, i
  Calculate over the entire video sequence:
    Mean and variance of the set of {Vq, i}
    Higher mean and lower variance  better overall video quality

## Slide 8: Discussion
Propose to add video quality evaluation metrics for consideration by Rmcat WG. Desirable features of the metrics should include:
  Good correlation with subjective video quality perception
  Combine different parameters to provide an integrated look at video QoE impact
  Relatively simple to calculate based on data from network simulations
  Ideally, based on published standards
Subjective quality evaluation is hard to organize and execute, especially in a contribution evaluation phase
Common objective evaluation metrics of video quality
  Easier to use in proposal evaluations,
  Full-reference & Non-reference: latter may be more suited for RMCAT evaluation
ITU-T Rec.G.1070 based NR VQ metrics designed for video conferencing applications
  Additionally, this doesn’t require compressed bitstream inspection, etc.: algorithm inputs are high level, e.g. throughput, packet loss rate, etc.
Soliciting feedback from group on defining consideration for video quality metrics as part of evaluation criteria for congestion control algorithms?  Current phase
For further consideration: Could VQ be exploited by congestion control algorithms?
  Potential for incorporating video quality information into RTCP XRBLOCK reports?
   (Later phase)

## Slide 9
Annex

## Slide 10: Background
Rmcat WG is dealing with congestion control for Internet data considering interactive point-to-point real-time multimedia services over RTP
Requirements for congestion control algorithms are defined considering
  Low delay
  Semi-Reliable data delivery
  Fairness to other flows
  Adaptation to network conditions
Metrics for congestion control are defined to be
  Delay, throughput, minimizing transmission rates oscillations, reactivity to transient events and packet losses and discards
Evaluation Criteria for congestion control algorithms have been defined considering
  Avoiding Congestion Collapse
  Stability
  Media Traffic
  Startup Behavior
  Diverse Environments
  Varying Path Characteristics
  Reacting to Transient Events or Interruptions
  Fairness with Similar Cross Traffic
  Impact on Cross Traffic
  Extensions to RTP/RTCP

## Slide 11: Video Quality Variation w/ Network Conditions Variation
Source: R-G Cheng et al., “Measurement and Analysis of Skype Video Traffic,” APWCS 2008.
PSNRloss for different network bandwidth limitations
PSNRloss for different packet loss rate

## Slide 12: Impact of Throughput Variation on Video Conferencing Applications
Source: L. De Cicco et al., “Skype Video Responsiveness to Bandwidth Variation,” ACM NOSSDAV 2008.

## Slide 13: Video Quality Evaluation: Introduction
Quality of Experience
  The overall experience the consumer has when accessing and using provided video services
Quantifying Video Quality
  Mean Opinion Score (MOS)
    Subjectively done: recruit a group of people to watch a set of video clips and give a numeric score to each clip
    Automatically done: design algorithms to estimate a MOS based on characteristics of media stream, network, device, etc.
Video Quality Issues
  Video creation, video encoding/transcoding, video transmission, video display

## Slide 14: Video Quality Issues
Video blockiness (encoding)
Video blurriness (capturing/encoding)
Video losses (transmission)
Video jerkiness (transmission/encoding/display)
Video freezing/rebuffering (transmission)
A/V sync problem (transmission/encoding)
Blockiness vs. blurriness

## Slide 15: PSNR (Peak Signal-to-Noise Ratio)
Most commonly used metric to measure the quality of reconstruction of lossy compression codecs
  Typically values between 30~50 dB, higher is better

## Slide 16: MS-SSIM
Luminance l(x, y)
Contrast c(x,y)
Structure s(x,y)
Typical values between 0.8~1, higher is better

## Slide 17: PEVQ
Output PEVQ MOS ranging from 1 (bad)~5 (excellent)
Distortion Indicators: Delay, Brightness, Contrast, PSNR, Jerkiness, Blur, Blockiness, Frame skips and freezes, Temporal Activity and spatial complexity

## Slide 18: ITU-T SG12 No-Reference Objective Standards
Consented or Approved documents shown in black
Targeted Applications: IPTV services; non-adaptive streaming; non-interactive
P.1201.x – multimedia QoE; P.1202.x – video QoE
Targeted protocols: non-HTTP (RTP, TS-on UDP, etc.)
Bit Stream
Packet Headers
Decoded Video
P.1201.1 (lbr*) P.1201.2 (hbr*)
P.1202.1 (lbr*) P.1202.2 mode 1 (hbr*)
J.bitvqm,J.mm-noref, J.noref, VQEG-JEG Hybrid Project
Inputs
P.1202.2 mode 2 (hbr*)
* lbr- low bit rate hbr- high bit rate

## Slide 19: P.120x.x Video Impairment Model
P.1202 Approach
  Design a metric for evaluating quality in specific instance; i.e., IPTV services
  This significantly constrains the problem, and should make the solution much more feasible
    Known video encoder; encoder output available
    Known channel; impairment pattern available
Four main video distortions accounted for
  Compression Artifacts
    Due to lossy encoding
  Slicing Artifacts
    Due to Packet Loss Concealment (PLC) of lost packets
  Freezing Artifacts
    Due to PLC replacing erroneous frames with last good frame (“freezing with skipping”)
  Rebuffering Artifacts
    Due to PLC repeating a frame until frame reception recommences (“freezing without skipping / spinning wheel”)

## Slide 20: P.1202 (ex. P.NBAMS)
Two application areas :
P.1202.1,"lower resolution mode”:
  Same as P1201.1:
    i.e., QCIF-QVGA-HVGA, mostly for mobile TV and Streaming
P.1202.2, "higher resolution mode”:
  Linear broadcast TV & Video on-demand:
    Still under Study

## Slide 21: P.1202 (ex. P.NBAMS)
Packet Headers and bitstream input only
Not intended for codec evaluation
Not intended for streams with significant rate adaptation
Video Pearson correlation of 0.918 for P.1202.1 (982 samples)
Validated Test Factors |  | 
Recommendation | P.1202.1 | P.1202.2
Audio BR | NA | NA
Video BR | 0.05 – 6 Mbps | Under study
Packet loss |  | Under study
Re-buffering |  | 
Video Resolution | HVGA, QVGA, QCIF | Under study
Video encoding | H.264/AVC baseline | Under study
FR’s and key frame rates | Frame rate 5-30 Hz GOP lengths 2-10s | Under study
Protocol | UDP-based | Under study
Protocols not tested* | TCP-based | Under study
* (can be used, but may not be reliable)