## Slide 1
IETF88 Vancouver
  Congestion control for video and priority drops
  Background for
  draft-lai-tsvwg-normalizer-02.txt
  Toerless Eckert, eckert@cisco.com
I
LTR
P
dP

## Slide 2: Summary
draft-lai-tsvwg-normalizer-02.txt discusses key problem of larger solution
  Provide overview of larger solution here: Priority dropping
Interest for priority dropping due to p2p video resilience work
Overlap/beneft also for p2mp switched video
What can the network do ?
Consider how priority drops can be beneficial for CC and video quality
What is missing ?

## Slide 3: Use case 1: RT P2P video resilience A historical perspective
Loss of video packets during congestion happen.. and is unavoidable
  Today Internet traffic far from ideal congestion control
  Even with ideal congestion control: bad competing traffic, burst collisions,…
Mitigation:
  Retransmission (incurs delay ~RTT)
  Concealment (in video layer of application, interpolation == delay)
  Redundancy/Protection/FEC
Optimize Protection by taking video packet priority into account
  Loss of higher priority video packet has bigger impact on quality
  Streaming: I (high), P (medium), B (low), Conferencing: LTRF (high), P (medium), discardable P (low)
  Use unequal protection: more FEC for I/LTRF, less for P, none for B/dP
  BW-cost of FEC still high, efficiency limited by acceptable delay,
  Effectiveness limited by loss profile (bursty loss = hard to protect with low delay)
Dear network, please drop only low priority video packets
  Avoids FEC downsides: overhead, limited effectiveness, delay

## Slide 4: Use case 2: RT P2MP video rate-adaptation.
Switched MCU video conference:
  Sender -> switching MCU -> multiple receivers
Congestion from MCU to receiver requires rate-adaptation at MCU
  switching MCU == no codec layer == no transrating/transcoding.
  Rate-adaptation via:
    Shaping (== delay == bad)
    Select next-best spatial encoded video from sender (eg: QCIF, CIF, 4CIF, 16CIF,…)
    Drop frames from that encoded video to match available rate.
      Hierarchical temporal encoding with discardable P-frames.
      Dropping dP frames minimizes visual impact.
Priority dropping in network can improve this:
  Unavoidable network drops are like the P2P use case (bad or FEC,…)
    Faster: low-prio dropping in network will drop low priority immediately.
  MCU dropped packets (“holes”) make flow more bursty == difficult for CC.
    Loss rate on these flows may get higher or achievable rate lower

## Slide 5: Proactive relying on low-priority drops: Better than no drops ?!
Minimizing drops via rate-control impacts throughput
  Especially with bursty traffic.
  RT video traffic has great justification/need for burstyness
Example 1: Compare delay-variation/ECN with eg: PCN
  PCN can achieve lower loss than delay-variation/ECN rate-control alone.
  PCN “Headroom” is unused bandwidth available to bursts.
Example 2: Similar effects for conservative rate-control
  The less rate-control “probes” the limit to loss, the less loss there will be.
  And the less throughput.
Claim 1 (intra-flow): Visual impact of loosing low-priority video packet may be lower than a reduction in overall bitrate of video flow.
Claim 2 (inter flow): Aggregate quality result is better when high-prioirty packets can burst more without loss – at the expense of low-priority packets sometimes getting dropped.

## Slide 6: So, what could a network do ?
Assume we have video packets marked with priority
Queues in network devices can quite effectively drop low priority packets over high priority packets.
  Leveraging existing HW queue options: Droptail profiles / WRED
  Example with three priorities:
    high (20% bitrate of flows), normal (60% bitrate of flows), low (20% bitrate of flows)
      Rates are longer term average – eg: over ½ second
    Queue:
      high priority packets dropped on 100% queue length
      Normal priority packets dropped on 90% queue length
      Low priority packets dropped on 40% queue length
    On any loss under 10% can achieve >> 99.9% loss in only low priority packets
    On loss at 40%, can achieve “ideal loss” – all low priority, 20% medium priority, no high priority.
Guess: the more priorities to distinguish, the less crisp the results.

## Slide 7: So, what is missing then ?
Useful priority markings
  DSCP difficult/overloaded – if priority dropping would be useful for N existing types of traffic (realtime video, streaming video, market-data/telemetry,…) we would need at least 3 * N DSCP.
  For video, RTP header extension with “drop priority” would be ?ideal?
    RTP header extension would require onpath signaling to let routers know (eg: MALICE).
Application support
  Mark the priority of packets
  Encode video to best utilize packet priorities.
  Optimize rate-adaptation & congestion control if priority dropping is supported.
    If loss in network is only in low-priority packets, application know that congestion happens at a point in network that supports it.
    Better/faster upspeeding
    less need to shape/avod bursts
    No protection overhead, … adjusted CC parameters (longer rate averaging)
Fairness, Normalization, standard profiles ?

## Slide 8: Fairness ?
Unfairness with existing queuing setups:
  The lower the average priority in a flow, the more loss it will see vs. other flows
  No motivation for applications to honestly mark priority of packets
  Great incentive to mark packets with only high-priority
draft-lai-tsvwg-normalizer-02.txt solves this problem
  Router analyzes distribution of priorities in flow.
  Remaps priorities (internally, not visible in packet) so that distirbution of priorities match a normalized profile (eg: 20% high, 60% medium, 20% low).
  All flows now compete fairly in the queue and see same amount of drops.
  Running code. But unclear if this scales to higher end routers
More generic approach ?
  Agree on a simple standard profile 20/60/20 ?
  Perform normalization or filtering only on “trust” edge
    Exactly like for any other QoS function.

## Slide 9
Background:
some
simulation results
Notes: 9

## Slide 10: Droptail all packet priorities can fill whole queue
Wrong labels:
red = dP
Green = P
blue = LTRF
~10% dropped
Measured: # of packets dropped every 0.1 second

## Slide 11: Threshold_dP=90%

## Slide 12: Threshold_dP=50%

## Slide 13: Threshold_dP=40%

## Slide 14: Threshold_dP=30%

## Slide 15: Varying drop thresholds for dP-Frames percent of queue-length
Droptail