## Slide 1
Jaehoon (Paul) Jeong, Hyoungshick Kim, and Jung-Soo Park
Sungkyunkwan University & ETRI
Requirements for Security Services based on Software-Defined Networking draft-jeong-i2nsf-sdn-security-services-00
IETF 91, Honolulu, HI, November 13, 2014

## Slide 2
  Contents
  I
Introduction
  V
Use Cases
  II
SDN-Based Security Services
  III
Objectives
  IV
Requirements
  VI
Discussion

## Slide 3: Standardization Status in ITU-T
Working Item in Study Group 17 (SG 17), Question 6 (Q.6) in ITU-T
  Our proposal for“Requirements for Security Services based on Software-Defined Networking”was accepted as a working item in September Meeting in 2014.
Scope of the Draft in SG 17.
  Classify the network resources for SDN-based security services.
  Define the requirements for SDN-based security services.
  Define the enhanced framework to support SDN-based security services.
  Define use cases for security services based on SDN.

## Slide 4: Motivation
Legacy Firewall
  Firewall inspects packets that attempt to cross a network boundary.
  Firewall rejects any illegal packets such as
    Incoming requests to open illegal TCP connections,
    Packets of other illegal types (e.g., UDP and ICMP), and
    IP datagrams with illegal IP addresses (or ports).
  Firewall provides security at the loss of flexibility and the cost of network administration.

## Slide 5: Challenges in Firewall
Cost
  The cost of adding firewalls to routers is substantial.
Performance
  Firewalls are often slower than the link speed of their network interfaces.
Management
  Managing access control dynamically across hundreds of network elements is a challenge.
Policy
  It is difficult to describe what are permitted and denied flows within the specific organization.
Binding
  Packet-based access mechanism is not enough in practice since the basic unit of access control is usually user or application.
    e.g., Skype connections for specific users are open.

## Slide 6: Centralized Network Firewall based on Software-Defined Networking (SDN)
Centralized Network Firewall
  Firewall rules can be managed flexibly by a centralized server.
  SDN protocols can be used for a standard interface between firewall applications and switches.
Public network
Private network
Firewall
Switches
add or delete
rules
<Match, Action>
<Match, Action>
…

## Slide 7: Expectations for SDN-Based Firewall
Cost
  Ideally, one single firewall is enough.
Performance
  Firewalls can adaptively be deployed depending on network conditions.
Management
  Firewall rules can dynamically be added with new attacks.
Policy
  Centralized view might be helpful to determine security policies.
Binding
  Application level rules can be defined by software.

## Slide 8: SDN-Based Security Services
DDoS-Attack Mitigator
Firewall
SDN Controller
Switch2
Switch3
Switch1
Install new rules
(e.g., drop packets with suspicious patterns)
Incoming packets
Incoming packets

## Slide 9: High-Level Architecture for SDN-Based Security Services
Multi-Layer Management Functions
Security Application
(e.g., Firewall, DDoS-Attack Mitigation)
Application Support
Orchestration
Abstraction
Control Support
Data Transport and Processing
Application Layer
SDN Control Layer
Resource Layer
Resource-Control Interface
Application-Control Interface

## Slide 10: Objectives
Prompt reaction to new network attacks
  SDN-based security services allow private networks to defend themselves against new sophisticated network attacks.
Autonomous defense from network attacks
  SDN-based security services identify the category of network attack (e.g., worms and DDoS attacks).
  They take counteraction for the defense without the intervention of network administrators.
Network-load-aware resource allocation
  SDN-based security services measure the overhead of resources for security services.
  They dynamically select resources considering load balance for the maximum network performance.

## Slide 11: Requirements
The support of the programmability of network resources to mitigate network attacks.
The support of an application interface allowing the management of access control policies in an autonomous and prompt manner.
The support of a resource-control interface for control of network resources to mitigate network attacks.
The support of logically centralized control of network resources to mitigate network attacks.

## Slide 12: Use Cases
Centralized Firewall System
  This is for malware packets.
Centralized DDoS-Attack Mitigator
  This is for DDoS-attack packets.

## Slide 13: Centralized Firewall System (1/2)
Firewall
SDN Controller
Switch2
Switch3
Switch1
Malware packet
1. Switch1 forwards an unknown flow’s packet to Firewall via SDN Controller.
2. Firewall investigates the packet.
3. Firewall regards it as a malware packet with suspicious patterns.

## Slide 14: Centralized Firewall System (2/2)
Firewall
SDN Controller
Switch2
Switch3
Switch1
Install new rules
(e.g., drop packets with suspicious patterns)
Incoming packets
Incoming packets
Report a malware’s packet to SDN Controller
The malware’s packets are dropped by switches

## Slide 15: Centralized DDoS-Attack Mitigator (1/2)
DDoS-Attack Mitigator
SDN Controller
Switch2
Switch3
Switch1
DDoS-attack packets
1. Switch1 suspects a flow’s packets with inter-arrival patterns.
2. Switch1 reports this flow to DDoS-Attack Mitigator via SDN Controller.
3. DDoS-Attack Mitigator computes a separate path for the suspicious flow.

## Slide 16: Centralized DDoS-Attack Mitigator (2/2)
DDoS-Attack Mitigator
SDN Controller
Switch2
Switch3
Switch1
Install new rules
(e.g., forward packets with suspicious inter-arrival patterns to a separate path with random drop)
Incoming packets
Undropped Incoming packets
Report the suspicious flow to SDN Controller
The suspicious flow’s packets are randomly dropped by Switch3 on the separate path

## Slide 17: Discussion
Direction of This Draft
  Develop SDN-based Security Services (e.g., Firewall and DDoS-Attack Mitigator) including API.
  Include other Security Services, such as Preventing the leakage of internal traffic into the outside networks.
Direction of our ITU-T SG 17 Draft
  Develop Security Scenarios and Requirements for ITU-T Y.3300 (Framework of Software-Defined Networking).
Thanks for your attention.
Any Comments or Questions?