## Slide 1: RFC6374 Synonymous Flow Labels draft-bryant-mpls-synonymous-flow-labels-01
S. Bryant, G. Swallow & S. Sivabalan : Cisco
G. Mirsky : Ericsson
M. Chen & Z. Li :Huawei

## Slide 2: The RFC6374 Problem(s) In Regular MPLS
PE1
PE2
PE4
PE4
ECMP Reorder
Linecard Co-ordination
Source Discrimination
Internal
Synch

## Slide 3: Synonymous Flow Label
A synonymous flow label (SFL) is a label that causes the Egress LSR to perform a previously agreed action in addition to processing and delivering the packet in exactly the same way as the label that it is synonymous with (except if the action says otherwise).
The action may be increment a counter, log a packet, or anything else that is agreed between the MPLS peers.
The additional action that RF6374 needs is the incrementing of a flow specific counter, something that many LSRs can already do!

## Slide 4: Other Possible Synonymous Actions
Record this packet
Get IPFIX to look at this packet
DPI this packet
Send this packet for DOS washing
…..

## Slide 5: Synonymous with Application Label
+-----------------+ +-----------------+
| | | |
| LSP | | LSP | <May be PHPed
| Label | | Label |
+-----------------+ +-----------------+
| | | |
| Application | | Synonymous Flow |
| Label | | Label |
+-----------------+ +-----------------+
| | | |
| Payload | | Payload |
| | | |
+-----------------+ +-----------------+
"Normal" Label Stack Label Stack with SFL

## Slide 6: Single Label Stack
+-----------------+
| |
| LSP | <= May be PHPed
| Label |
+-----------------+ +-----------------+
| | | | <= Synonymous with
| LSP | | Synonymous Flow | Explicit NULL
| Label | | Label |
+-----------------+ +-----------------+ <= Bottom of stack
| | | |
| Payload | | Payload |
| | | |
+-----------------+ +-----------------+
"Normal" Label Stack Label Stack with SFL

## Slide 7: Aggregate Label Stack
+-----------------+
| |
| LSP | < May be PHPed
| Lable |
+-----------------+ +-----------------+
| | | |
| LSP | | Agregate |
| Label | | SFL |
+-----------------+ +-----------------+
| | | |
| Application | | Application |
| Label | | Label |
+-----------------+ +-----------------+ <= Bottom of stack
| | | |
| Payload | | Payload |
| | | |
+-----------------+ +-----------------+
"Normal" Label Stack Label Stack with SFL

## Slide 8: ECMP
The addition of an SFL may cause a change to the path through the network due to the change in the packet entropy value. IF this is a problem
Always include the SFL or
Use an RFC6790 entropy label

## Slide 9: A Rose By any Other Name
adjective: synonymous
1. (of a word or phrase) having the same meaning as another word or phrase in the same language.
2. closely associated with or suggestive of something.
It has been suggested that definition (1) is not a good fit for what we are doing. Definition (2) works or we could move to something like “shadow”.

## Slide 10: Next steps
Revisit the requirements draft (draft-bryant-mpls-flow-ident)
  Is that correct and complete?
  Do we publish, or merge into this. or let the draft die?
Decide if this draft the approach we wish to follow
  How much more should the authors do before handing control the the WG.
Design the control system.
  Let’s discuss on the list
  We will have a draft(s) for Japan, and welcome inputs from the WG.