## Slide 1: draft-kompella-mpls-larp MPLS RT review
Kireeti Kompella, Balaji Rajagopalan; George Swallow
IETF 93/Prague 2015

## Slide 2: Summary of MPLS RT Review
1) Need demonstrable use case for labeled ARP
  MPLS in the data center (MPLS Fabric)
  MPLS in the access
2) Need to fill in more details on restart scenarios
  How should the client and server behave
  What should the client expect from server (and vice versa)
3) Need bidirectional connectivity to the client
4) Need to give more details on how L-ARP clients deal with multiple responses for the same target protocol address
  Multi-homed clients
  Clients on a LAN

## Slide 3: Use Case/Applicability for L-ARP
Use case: MPLS in the data center
  The draft refers to an as-yet-unwritten draft on an “MPLS Fabric”
  Here, the L-ARP client is a compute server participating in an MPLS underlay
  Writing this up would present a use case for L-ARP
  Will be done
Use case: MPLS in the access
  A D-SLAM/OLT/… that wants to participate in an MPLS network can use L-ARP to do so
  This is not unlike the previous use case
  Can be added to the MPLS Fabric draft

## Slide 4: Restart Scenarios
In “regular” ARP, the protocol-hardware address (i.e., IP-MAC) binding is relatively stable; the hardware address is global
In L-ARP, the binding could change; the hardware address is local
Thus, care is required to keep the client and server in sync; this is most obvious in restart situations
We will fill in details on this in the next rev

## Slide 5: Bidirectional MPLS Connectivity
A device X wanting MPLS connectivity to another device Y can use L-ARP to learn the label to use (L1) for sending
  But what label (L2) should X expect to receive packets?
The previous hop (T) needs to allocate a label for X
  The label that X receives may be NULL (PHP) or not (UHP)
  In the former case, X doesn’t need to know
  The latter case can be handled by Labeled DHCP
    There was a short discussion of this on the mailing list a year ago
  We’ll add text to lay out the issue and discuss solutions
X
Y
T
…
L1
?

## Slide 6: Handling Multiple Responses
An L-ARP client may receive multiple responses to L-ARP requests for a particular protocol address (IP)
  This can happen if the client is on a LAN with multiple servers that have MPLS reachability to the target IP
  This can also happen if the client is multi-homed
The paradigm used in L-ARP is that of “proxy ARP”
  Thus, the L-ARP server is usually not the target
The “attribute” TLV contains a metric for the client to make an intelligent choice in this situation
  The authors assumed that the use of metrics was obvious; it appears this isn’t quite so obvious
  We’ll add verbiage to explain this in more detail

## Slide 7: Next Steps
1) New revision of the draft addressing these issues
  Couple of weeks post-IETF93
2) MPLS Fabric draft describing use cases
  Similar time frame, possibly slightly longer
Hopefully, these two actions will satisfy the reviews
  With the reviewers’ sign-off, we will republish as a WG document