## Slide 1: Framework for Abstraction and Control of Transport Networks
draft-ceccarelli-teas-actn-framework-00
IETF 93 – Prague
Daniele Ceccarelli (Ericsson)
Young Lee (Huawei)
Daniel King (Lancaster-University)
Sergio Belotti (Alcatel-Lucent)
Luyuan Fang (Microsoft)
Dhruv Dhody (Huawei)
Diego Lopez (Telefonica)

## Slide 2: Draft-status
Respin of draft-ceccarelli-actn-framework-07
  v00 published on Jan 2014
Requirements moved
  To: draft-lee-teas-actn-requirements-00
Use cases moved
  To: draft-lee-teas-actn-requirements-00

## Slide 3: Architecture
PNC
ACTN i/f
PNC
PNC
PNC
PNC
MDSC
MDSC
MDSC
CNC
CNC
CNC
PNC (Physical Network Controller)
Is a domain control/management entity (e.g., GMPLS CP, PCE, OF controller, NMS/EMS)
It sits at the bottom of the hierarchy of controllers and directly speaks to the nodes.
It is responsible for domain-specific network control operations such as configuring network elements, provisioning, monitoring, protection and recovery of the networks in charge.
It provides the MDSC with an abstract view of its domain topology and services

## Slide 4: Architecture
PNC
PNC
PNC
PNC
PNC
MDSC
MDSC
MDSC
CNC
CNC
CNC
MDSC (Multi Domain Service Controller)
Coordinator/orchestrator responsible for supporting customers’ virtual networks creation, modification and deletion
Allows for Multi-domain coordination/orchestration among PNCs
Creates end-to-end paths and services
Allows for a hierarchy of MDSCs for administrative and scalability issues.

## Slide 5
PNC
PNC
PNC
PNC
PNC
MDSC
MDSC
MDSC
CNC
CNC
CNC
CNC (Customer Network Controller)
is responsible for creating VN service instantiation
providing service/application requirement including endpoint information to network operators.
Examples of Customers are VPNs, MVNO, ISP, etc.
VPN customer
NW Mobile customer
ISP on-demand NW service customer

## Slide 6: Controllers Functionalities
PNC
PNC
PNC
PNC
PNC
MDSC
MDSC
MDSC
CNC
CNC
CNC
Multi domain coordination function
Virtualizer function
Customer mapping function

## Slide 7: Not just SDN
SDN
MDSC
PCE
NMS
SDN
PCEP+GMPLS
OF
PCEP/SR
OF
PCEP/RSVP-TE
NETCONF/Yang
The ACTN hierarchy is suitable for non homogeneous networks
  Different SDN control methods for packet and optical domains (e.g. SR or OF)
  Different control methods for packet and optical SDN and non-SDN (e.g. SR, GMPLS, RSVP-TE, NMS)

## Slide 8: Next Steps
IETF 92 output: TEAS is the home for ACTN FWK work
Draft ready for WG adoption
Keep alignment with requirements and use cases draft(s)
ACTN work next steps:
  Info model (TEAS?)
  Protocols extensions (!TEAS)