## Slide 1: IETF 94 Yokohama
draft-finn-detnet-problem-statement
Norm Finn, Pascal Thubert
DetNet problem statement

## Slide 2: Doc charter
This effort will establish the deployment environment and deterministic network requirements.
The working group will document which deployment environments and types of topologies are within (or outside) the scope of the DetNet architecture.

## Slide 3: Deployment environment(s)
Extending beyond the LAN
Applies to RAN, SmartGrid, Pro-Audio, …
Extent of the network TBD (multiple admin, WAN…)
Enable a fully scheduled operation orchestrated by a central controller
May support a more distributed operation with probably lesser capabilities

## Slide 4: Requirements
DetNet should thus produce the complete SDN architecture with describes at a high level the interaction and data models to:
report the topology and device capabilities to the central controller;
request a path setup for a new flow with particular characteristics over the service interface and control it through its life cycle;
signal the new path to the devices, modify it to cope with various events such as loss of a link, update it and tear it down;
expose the status of the path to the end devices (UNI interface)
provide additional reliability through redundancy, in particular with packet replication and elimination;
indicate the flows and packet sequences in-band with the flows;

## Slide 5: Doc structure
2. Terminology . . . . . . . . . . . . . . . . . . . . . . . . . 5 3. On Deterministic Networking . . . . . . . . . . . . . . . . . 5 4. Related IETF work . . . . . . . . . . . . . . . . . . . . . . 7
4.1. Deterministic PHB . . . . . . . . . . . . . . . . . . . . 7
4.2. 6TiSCH . . . . . . . . . . . . . . . . . . . . . . . . . 7 5. Related work in other standards organizations . . . . . . . . 8
5.1. Bridged solutions . . . . . . . . . . . . . . . . . . . . 8
5.2. Queuing and shaping . . . . . . . . . . . . . . . . . . . 8 6. Problem Statement . . . . . . . . . . . . . . . . . . . . . . 9
6.1. DetNet architecture . . . . . . . . . . . . . . . . . . . 9
6.2. Flow Characterization . . . . . . . . . . . . . . . . . . 11
6.3. Centralized Path Computation and Installation . . . . . . 11
6.4. Distributed Path Setup . . . . . . . . . . . . . . . . . 11
6.5. Duplicated data format . . . . . . . . . . . . . . . . . 11

## Slide 6: Out of scope
Bridging operations
  Already defined at IEEE 802.1 TSN
Time Sync
  Already defined at IEEE (PTP 802.1AS or 1588)
  Or other groups (TICTOC, NTP)
Shapers and queue management
  Already defined at IEEE

## Slide 7: DetNet Architecture
Network
Controller (PCE)
Sender
(Talker)
NIC
NIC
Service
Interface (northbound)
Receiver
(Listener)
Control Management
Interface (southbound)
UNI
I/F
4) State installation
1) Topology and Capabilities reporting
5) Shaping and Per-Hop Behavior
Packet with Flow ID
UNI
I/F
3) Controller
computes paths
2) Application Specifies Requirements
Application / Service Controller

## Slide 8: In scope
Interaction Models
  Centralized architecture (distributed also?)
  SouthBound flows
  UNI (LMI++, CIR++ …)
Information Models
  TSpec (flow characterization)
  Data model for per-flow state (buffers, Qs, timing)
  Flow identification in packets (FlowID, seq#, time)
  Data Plane transport (MPLS, IPv6…)
  Data plane OAMs