## Slide 1: IETF 94 Yokohama
draft-finn-detnet-architecture
Norm Finn, Pascal Thubert, Michael Johas-Teener
DetNet Architecture

## Slide 2: DetNet Architecture
Objective/purpose of document
  Goals
  Non-goals
Current status
Essential aspects of the architecture
Open issues questions/discussion
Plans
Open discussion

## Slide 3: Objectives / goals
To define an architecture that:
  Provides assured maximum latency and extremely low packet loss rates for fixed-bandwidth critical streams
  Across a mixed bridged and routed network
  Taking advantage of IEEE 802.1 TSN standards
  Without disrupting existing Qualities of Service,
  While adding and/or modifying as few concepts, hardware requirements and protocols as possible.

## Slide 4: Objectives / non-goals
Critical streams have fixed bandwidth; congestion control via feedback / throttling is not an option.
Tunneling through L3 networks to connect L2 TSN domains is not precluded, but is not a specific goal; target applications’ networks are too big for L2 connectivity.
Precise time synchronization is typically required by the target applications, and by some proposed DetNet queuing techniques, but is not an objective of DetNet.

## Slide 5: Current status
draft-finn-detnet-architecture-03 uploaded on 2 Nov; minor corrections/clarifications from (expired) version 02.

## Slide 6: Essential aspects of architecture
Reservation/enforcement: Network resources are reserved and various forms of data plane queuing/shaping/scheduling are configured along a stream’s path to ensure worst-case latency and zero congestion loss.
Seamless redundancy: Sequentialized streams can be sent over divergent and/or pinned-down paths and reassembled at intermediate points, or at/near the destination(s).
Defense: The effects of a misbehaving talker / bridge / router must be minimized.

## Slide 7: Essential aspects of architecture
One size does not fit all. Different applications and verticals make different selections of techniques.
Reservation model includes Applications Controllers requesting QoS for streams from a Network Controller.

## Slide 8: Open issues
Are the existing and in-progress shapers and schedulers necessary? Sufficient?
Are DiffServ techniques adequate? Shall we define IntServ techniques?
Which techniques for stream ID and sequencing for QoS and pinned-down paths are suitable in a mixed bridged and routed network?
  L2 addresses? L3 5-tuple or deeper? MPLS labels?
Is a peer-to-peer L2/L3 reservation protocol, working without a central controller, needed?
  If so, shall we base it on IETF RSVP? IEEE MSRP?

## Slide 9: Plans
Decide whether draft-finn-architecture is a suitable starting point for an architecture draft for the DetNet WG.
If so, make whatever changes are needed to make the draft suitable for adoption by the DetNet WG.

## Slide 10: Open Discussion
Blindfold? Cigarette? Ready! Aim!