## Slide 1: IETF 95 – Buenos Aires April 2016
A YANG Data Model for
MPLS Base and Static LSPs
(draft-saad-mpls-static-yang-02)
            Tarek Saad (Cisco) -- Presenter
            Kamran Raza (Cisco)
            Rakesh Gandhi (Cisco)
            Xufeng Liu (Ericsson)
            Vishnu Pavan Beeram (Juniper)
            Himanshu Shah (Ciena)
            Jescia Chen (Huawei)
            Raqib Jones (Brocade)
            Bin Wen (Comcast)

## Slide 2: Background
The goal of this draft is to specify two YANG models:
  MPLS Base
  MPLS Static LSPs
The MPLS base YANG module serves as a base framework for configuring and managing an MPLS switching subsystem
  Augments the core routing data model [I-D.ietf-netmod-routing-cfg] with additional data specific to MPLS switching
  Defines Base MPLS types and MPLS interface list and properties
  Augmentation by other MPLS protocol modules expected
    TE, LDP, and LSP static
The MPLS Static LSP module:
  Augments the MPLS base YANG module
  Defines parameters related to MPLS Static LSPs.

## Slide 3: Update
Draft initially introduced at IETF-94, Yokohama
Update to augmentation path to reflect recent change in core routing data model [I-D.ietf-netmod-routing-cfg] (removal of routing-instance)
MPLS RT Review [-02 Version] is underway
  Reviewers: Sam Aldrin, Huub van Helvoort, Carlos Pignataro, and Mach Chen
  Received comments from Huub
Interest in generalizing the Static LSP Model to non-MPLS technologies
  Rather than defining Static LSP models for each technology MPLS, OTN, WDM

## Slide 4: Open Issue #1 Static LSP model for non-MPLS Technologies
Issue - current Static LSP model is MPLS centric
  Need Static LSPs functions for multiple other technologies, OTN, WDM, etc.
Proposal – regroup/restructure of MPLS Static LSP module:
  Decouple Static LSP model from MPLS technology
    Abstracting it into technology agnostic data model (similar to TE generic model)
  Utilize model attachment capability (e.g. mount) to apply generic Static LSP model to different technologies
  Augment generic Static LSP model with technology specific data

## Slide 5: Open Issue #2 MPLS-RT reviewer comments (from Huub)
Comment#1: draft should be split into two separate documents:
  one for describing the MPLS base YANG module, and
  one for describing the MPLS Static LSP module
Comments/other: nits, will be addressed
Proposal/resolution-
  Authors agree to divide the two into separate drafts
  This facilitates generalizing into generic Static LSP model

## Slide 6: Open Issue #2 MPLS-RT reviewer comments (from Carlos)
Comment#1: suggest draft to be split into two separate documents
Comment#1: use of “loadshare”
  Relevant for multiple paths with unequal weights
Comments/other: nits, will be addresses
Question: Does this model allow the creation of a Label Stack, in which there is a label with index 1, a label with index 5, and nothing defined in between?
  Answer: Yes, as currently defined, the index is simply a unique key in the list and not the offset in label stack

## Slide 7: Next Steps
Address outstanding comments
Soliciting more comments MPLS RT reviewers and WG
Close on approach to generalize Static LSP model to multiple technologies

## Slide 8: Backup Slides

## Slide 9: MPLS Static LSPs: Building Blocks (2)
In-Segment
Op
Out-Segment
ip-prefix,
or
local-label
impose
swap
pop
pop-impose*
pop-and-lookup
.
.
.

## Slide 10: MPLS Static LSPs: Building Blocks
An MPLS Static LSP is defined as an ordered set of following three:
  In-segment
  Operation
  Out-segment
In-Segment: Incoming segment of an LSP that is used as a lookup key for taking a forwarding action.
Operation: Operation (or action) that needs to be performed if lookup succeeds.
Out-Segment: Outgoing segment of an LSP that contains the actual forwarding information
  An Out-segment typically comprise 1 or more forwarding paths

## Slide 11: MPLS Static LSPs: Forwarding Path
Two types of forwarding paths defined:
  Simple path
    Uni-path
    Basic attributes
  Path List
    Multi-path
    Enhanced attributes (such as protection)
Path attributes:
  Table Id (next revision)
  Nexthop address
  Nexthop interface
  Label stack (0 or more labels)
  Load factor
  Role (primary / backup etc)
  Path-Id / Backup path-id for protection

## Slide 12: MPLS Base: Tree Diagram - Rev -00
module: ietf-mpls
augment /rt:routing/rt:routing-instance:
+--rw mpls
+--rw interface* [name]
+--rw name if:interface-ref
+--rw config
| +--rw enabled
+--ro state
+--ro enabled
mpls-base interface